## Slide 1: Jia Xing1,2, Bok H. Baek1, Siwei Li3, Chi-Tsan Wang1, Ge Song3, Siqi Ma1, Daniel Tong1 1George Mason University 2University of Tennessee-Knoxville 3Wuhan University
Efficient Estimation of NOx Emission variation using a Physically-Guided Variational Autoencoder

## Slide 2: Motivation
—combining multiple-observations for accurate prediction
Needs of Air Quality Forecasting
Limitation of Chemistry Transport Modeling
large variations in emissions
NO2 conc. (ug/m3) in North China Plain (Xing et al., ACP, 2020)
days from Jan 1st to Mar 31st 2020
Observation
Simulation with prior-emissions
Simulation with post-emissions
TROPOMI satellite observations show NO2 decreases (9.2% - 43.4%) among 20 cities in North America during 2020 pandemic
Goldberg et al., GRL, 2020

## Slide 3: Method-Variational Autoencoder (VAE)
encoder
q(z|x)
decoder
p(x|z)
emis.
z
prior NOx emissions
posterior NOx emissions
satellite-retrieved NO2 concentration
conc.
x
conc.
x’
Chemistry Transport Model
physically-informed
discrepancy
posterior-prior deviation
prediction-data deviation
a deep-generative model from observations to emissions
Xing, et al., ES&T 2022

## Slide 4: VAE framework
decoder
Meteorology
Adjusted NOx emissions
Observed NO2 concentration
Label
Input
encoder
Meteorology
Train
VAE
test
WRF-CMAQ
Meteorology’
Hypothesize NOx emissions
Simulated NO2 concentration
Predicted NO2 concentration
Step1: Pre-train decoder
Step2: Train encoder
Prior NOx emissions
Posterior NOx emissions
Train
Test
Step3: Apply VAE
Input
Input
Output
Forward model
Backward model
Surface NO2 concentration

## Slide 5: Model structure
CNN: convolution network; LSTM: long short term memory; U-Net structure (2-layers): a u-shaped architecture with a down sample function (max pooling) and a deconvolution function (up convolution); MLP: multiple layers of perceptrons with threshold activation; pReLU: the parametric rectified linear unit is used as the activation function
Concatenate
LSTM
LSTM
LSTM
LSTM
U-Net
CNN
pReLU
CNN
pReLU
CNN
MLP
Initial NO2 concentration
Cconc.= 1
2-meter temperature
PBL height
Wind speed
Short-wave radiation
convective velocity scale
humidity
U wind
V wind
CMeteorology= 8
NOx emission
Cemis.= 1
NO2
CConc= 1
Decoder
Encorder
UNet: capture the cross-space interaction
LSTM: capture the temporal variation

## Slide 6
Model structure of VAE
Concatenate
LSTM
LSTM
LSTM
LSTM
U-Net
CNN
pReLU
CNN
pReLU
CNN
MLP
Initial NO2 concentration
Cconc.= 1
2-meter temperature
PBL height
Wind speed
Short-wave radiation
convective velocity scale
humidity
CMeteorology= 6
NOx emission
Cemis.= 1
NO2
CConc= 1
Decoder
Encorder
Objective function:
Kullback–Leibler divergence
VAE concept: use a variational distribution (with a known density function and an easy sampling process distribution) to approximate the complex true posterior distribution .
posterior-prior deviation
prediction-data deviation
L-curve to determine the hyperparameter (noted as α) which balances these two

## Slide 7: Dataset from WRF/CMAQ simulation
 | Decoder (pre-train) | Decoder | Encoder
Met. | Input | Input | Input
Emis. | Input | Input | Output
Conc | Output (CMAQ) | Output | Input (Satellite)
Conc-init | Input (CMAQ) | Input (Satellite) | Input (Satellite)
2019/2020 baseline
2019/2020 satellite-retrieved surface NO2 concentration (TROPOMI fused with AQS sites)
For decoder
For encoder
Three scenarios:
  2019 baseline
  2019 double NOx emissions
  2020 meteorology with 2019 emissions
  2020 meteorology with no anthropogenic emissions
US 12km conus domain

## Slide 8: Dataset from observations
LightGBM (tree-based) model is used to derive the spatially continuous surface NO2 concentration
NO2 column products from TROPOMI
Surface NO2 measurements from AQS (65% of total labels)
CMAQ modeled NO2 from rural data (35% of total labels)
Sample = 359456
R2 = 0.9898
day of year
day of week
elevation
surface temperature
dewpoint
surface pressure
boundary layer height
total precipitation
total evaporation
10m wind
relative humidity
satellite column
Satellite retrievals

## Slide 9
NO2 reduced significantly during March-April in 2020
Satellite retrieved surface-NO2 concentrations present the similar reduction shown in AQS, but slightly lower compared to AQS
Spring (March-May)
Observations
daily-series for ∆NO2 (2020 - 2019)
change ratio

## Slide 10
Performance of VAE-decoder (forward)
VAE-decoder
CMAQ
VAE-decoder
CMAQ
VAE-decoder
CMAQ
VAE-decoder
CMAQ
Day3
Day4
Day5
Day6
Day7
Day8
Day9
Day10
Day11
Day12
Day13
Day14
Day15
Day16
Day17
Day18
Day19
Day20
Day21
Day22
Day23
Day24
Day25
Day26
2020 March
Daily NO2 (ppb)
Day 3-26
RMSE<0.5; R2>0.9

## Slide 11
Performance of VAE-decoder (forward)
2019 base (train) NMB < 0.3
2020 base (test) NMB < 0.4
Daily NO2 in March (ppb) by state
Performance in test dataset is worse than training, more training data will be helpful to improve the VAE-decoder performance

## Slide 12
Understanding the feature impacts on NO2 concentration
modulating each feature one-by-one
T2：-2K
others：-20%
NO2 concentration is contributed by NOx emissions (Enox) and initial NO2 condition (Ino2)
Met variables will modulate the NO2 concentration sensitivity to NOx emissions
monthly mean (2019)

## Slide 13
Performance of VAE-encoder (backward)
sim with no emission changes as 2019
Spring ∆NO2 concentration (2020 – 2019)
VAE assimilated
Satellite retrieved
VAE successfully assimilated surface NO2 concentration towards satellite
∆daily NO2 concentration between 2020 and 2019

## Slide 14
Comparing the VAE-adjusted (top-down) emissions with activity-based estimation (bottom-up)
kt/month
∆NOx emissions (2020 – 2019)
Both captured the NOx emission reduction in Spring

## Slide 15
Adjusted emissions
West
Southwest
Great Plains
Mid-south
Northeast
Southeast
wild-fires

## Slide 16
Emission impacts on concentration by vertical layers
Enox1: surface
Enox2: layer 2-3
Enox3: layer >3
Sensitivity of upper emissions to NO2 concentration increases along with the height
based on sensitivity analysis using DeepCTM by reducing each feature by 20%

## Slide 17: Conclusion
VAE is suitable ML model to efficiently capture the emission variations from the observed concentrations
  VAE is easy to train and apply, with limited resources (CTM-free)
limitations still exist
  sector-level emissions, uncertainties from numerical model and observations

## Slide 18: Acknowledgement: support from NOAA, NASA, WHO, US-EPA, NIEHS, KEITI, KCP
Thank you for your attention!