## Slide 1: Spatiotemporal NH3 Emissions using a Physically-guided Variational Autoencoder (VAE) with Remote-sensing Observations
CMAS Conference 2023, Chapel Hill, NC | October 16~18, 2023
B.H. Baek1, Jia Xing1, Mark Shepard2, Siwei Li3, Chi-Tsan Wang1, Jesse Bash3, Enrico Dammers4, Karen Cady-Pereira5, Daniel Tong1
1George Mason University; 2Environment and Climate Change Canada; Wuhan University3; 4U.S. EPA : 5TNO : 6AER

## Slide 2: Motivation
NH3 : Animal manure, production, and Application of fertilizers
  Short lifetime of NH3 ( = 0.5-5 days or less)
  Deposited to the surfaces near its source with relatively high dry deposition.
  Ecosystem eutrophication
NH4+ : Neutralization process of acid gases (H2SO4, HNO3 and HCl) by NH3 at the surface on PMfine  2.5m
  NH4HSO4, [NH4]2SO4, [NH4]3H[SO4]2, NH4NO3, NH4Cl,,,,
  Role of degradation of visibility in the local area
  Longer lifetime of NH4+ approximately 5~10 days
  Ecosystem acidification from ammonium oxidation in the atmosphere
  Sensitive spatiotemporal patterns by meteorology, events, and acid gases.
Top-down vs. Bottom-up NH3 emissions are quite different
  Swine NH3 emissions from Iowa and NC relatively overestimated?
  Beef NH3 emissions from Texas, Kentucky, and Nebraska are the main NH3 in Central US
(Shepard et al., 2020)
Notes: Ammonia (NH3) is the most abundant alkaline gas in the atmosphere and has major impacts on air, soil, and water quality. Ammonia, in general, is relatively short-lived in the boundary layer, so its day-to-day atmospheric concentration levels over a region can vary greatly depending mainly on the meteorology (e.g. wind speed, temperature), episodic events (e.g. biomass burning, spreading of fertilizer), and concentration of reactant acid gases (e.g. nitric and sulfuric acid from NOx and SOx ) to produce a significant fraction (∼ 50 %) of the secondary fine particulate matter
Deposition of basic ammonia and ammonium-containing aerosols on land surfaces leads to acidification of the soil, when ammonium is oxidized (nitrified) to nitrate (NH+ 4 + 2O2 → NO−3 + 2H+ + H2O; Goulding, 2016). 2016). The protons generated from this reaction cause the acidification. Massive atmospheric deposition of NH3 adds reactive nitrogeninto water that can contribute to eutrophication.
NH3 observations in US are Ammonia Network Monitoring (AMoN) and several NH3 satellites products. AMoN is a great dataset but very sporatic and the satellite may not be accurate as AMoN but better spatial coverage.
Satellite observations of lower tropospheric ammonia have only been possible in the past decade through concurrent improvements in both the radiometric capabilities of infrared instruments on satellites and the radiative transfer forward modeling and inversion algorithms
CrIS is the newest of these operational satellites and has the lowest radiometric noise in the portion of the spectrum commonly used for ammonia retrievals over the glove
Comparing the model emission and GEM-MECH concentration fields would indicate that these differences are mainly due to the input emission fields
Another application of CrIS ammonia observations is emission estimates. Emission inventories are traditionally built from the bottom up, using emission factors and source locations to construct a complete inventory
Top-down satellite observations can be used to provide another source of emissions information and to supplement the inventories with more detailed information on hotspot locations and temporal variations (e.g. seasonal and inter-annual variations;

## Slide 3: DeepCTM-VAE Applications with Observations
Objectives
  Bottom-up NH3 Emissions Comparison against Top-down NH3 Emissions
  Understand the differences and identify the solution to enhance the bottom-up Inventory
Deep-Learning Chemical Transport Model (Decorder)
  Development of DeepCTM (forward) based on the CMAQ CONUS12 simulation to understand the non-linear relationship between emissions and air quality
Variational AutoEncoder (VAE) Applications with CrIS Remote-sensing and AQS Observations
  Development of VAE (Backward) over the U.S.
  Data Assimilation: Surface NH3 concentrations based on the Crls remote-sensing and monitoring observations.
  Development of top-down NH3 emissions inventory over the U.S. and compare them against the bottom-up emissions (USEPA NEI)

## Slide 4: Methodology
Chemical Transport Model (CTM) CMAQ Simulations based on the latest U.S.EPA 2017 NEI
  All emission sectors including the agricultural (ag) sector with livestock waste and fertilizers
Deep-learning DeepCTM development based on CTM simulations
  Forward (Decoder): Emissions  Concentrations
NASA/NOAA’s CrIS NH3 Fast Physical Retrieval (CFPR) level-2 daily average (ppbv) over the U.S.
  Applied globally to CrIs spectra from May 2012
Variational AutoEncoder (VAE) to estimate the top-down emissions based on the Crls NH3
  Backward (Encoder): Concentrations  Emissions
  Based on the knowledge from the Decorder, VAE can estimate the physically-informed top-down emissions based on the observations (satellite Crls NH3)
Comparison of the bottom-up and top-down emissions inventories
  Quantitative comparisons between the NH3 emissions over the U.S. domains
  Sector-level NH3 emissions corrections from Livestock wastes, Fertilizer, Wildfires, Onroad mobile sources, and so on
Notes: Suomi National Polar-orbiting Partnership (S-NPP) satellite on 28 October 2011 and on the NOAA-20 satellite on 29 November 2017.

## Slide 5: DeepCTM: Deep-Learning CTM
Study the impacts from the inputs (Emissions, Meteorology, Concentrations, and Time)
Computationally highly efficient (<2 minutes) to execute DeepCTM once the training of DeepCTM is complete
(Xing et al., ES&T, 2020)
UNet: capture the cross-space interaction
LSTM: capture the temporal variation
Concatenate
LSTM
LSTM
LSTM
LSTM
U-Net
CNN
pReLU
CNN
pReLU
CNN
MLP
2-meter temperature
PBL height
Wind speed
Short-wave radiation
convective velocity scale
humidity
U wind
V wind
LAI
VEG
Prep
terrain height
grid area scale
CMeteorology= 11
NH3 daily mean
Cemis.= 1
NH3 daily mean
CConc= 1
Decoder
Encoder
Cgeography= 2
Notes: CNN: convolution network
LSTM: long short term memory
U-Net structure (2-layers): a u-shaped architecture with a downsample function (max pooling) and a deconvolution function (up convolution)
MLP: multiple layers of perceptrons with threshold activation
pReLU: the parametric rectified linear unit is used as the activation function
Machine learning shows its strong ability to reveal the complex atmospheric chemistry system
  The efficiency of AQ forecasting can be enhanced with ML-built emission-concentration relationship
  Exceptional computational advantages which allows users to perform CTM applications under various scenarios
  The accuracy of AQ forecasting can be improved with ML-assimilated emissions and satellite observations
Instant responsive CTM with a rapid refreshed emissions under the national emergency responses.

## Slide 6
Performance of VAE-decoder (forward: emis->conc)
VAE-decoder
CMAQ
VAE-decoder
CMAQ
VAE-decoder
CMAQ
VAE-decoder
CMAQ
Day3
Day4
Day5
Day6
Day7
Day8
Day9
Day10
Day11
Day12
Day13
Day14
Day15
Day16
Day17
Day18
Day19
Day20
Day21
Day22
Day23
Day24
Day25
Day26
Daily NH3 (ppb)
June 2020: Day 3-27
RMSE<3.0; R2>0.8

## Slide 7
The Feature Impacts on NH3 Concentrations
modulating each feature one-by-one
T2：-2K
others：-20%
NH3 concentration is contributed by NH3 emissions (Enh3) and initial NH3 condition (Inh3)
Met variables will modulate the NH3 concentration sensitivity to NH3 emissions
DeepCTM exhibits high efficiency in identifying the dominant factor to photochemical formation
Monthly mean (2019)

## Slide 8: Variational AutoEncoder (VAE): Top-down Emissions
∆（Sim-Obs）
∆（Emis）
auto-grad
back propagation
Based on emission-concentration relationship from DeepCTM, we can accurately estimate the differences of emissions
Because of the in-depth knowledge over various impactors (emissions, meteorology, initial conc.), we can proportionally correct the emissions only.
Variational AutoEncoder (VAE)
(Xing et al., ES&T, 2022)

## Slide 9: CrIS Fast Physical Retrieval (CFPR) Algorithm for NH3
CrIS is most sensitive to NH3 between 950 and 700 mb (~0.5 to 3 km) with minimum 0.3 ppbv detectability
  Not equally sensitive in the vertical and varies from profile-to-profile
  Surface retrieved values are driven by sensitivity in the boundary layer
CFPR has been validated with U.S. AMoN (Ammonia Monitoring Network) and other ground–based FTIR (Fourier Transform Infrared) spectroscopy observations to determine the errors
  AMoN: Crls ~15% higher with a good correlation of r ~ 0.8 and a slope of 1.02
  FTIR: Crls ~30% higher (SD~40%)
Applications to data assimilations, data fusion and model-based emissions inversions for Confined Animal Feeding Operation (CAFO) facilities located remotely.
(Shepard et al., 2020)
 | Satellite | Spatial Resolution (km2) | Spatial Coverage | Temporal Coverage | Retrieved Quantity | Comments
NH3 | Cross-track Infrared Sounder (CrIS) (2012-2038) | 14 (diameter) | Global | Twice a day CrIS-SNPP @ ~13:30 (day) ~1:30 (night) CrIS-NOAA20@ ~14:25 (day) 2:25 (night) | Profile level volume mixing ratio values (ppbv) | Limited vertical resolution Version 1.6 Shephard et al., ACPD, 2020 CFPR CrIS SNPP : May 2012 to May 2021 CFPR CrIS NOAA : March 2019 to present
Notes: cross-track infrared sounder (CrIS) is a satellite instrument with a Fourier-transform spectrometer onboard the Suomi National Polar-orbiting Partnership (NPP) satellite, which is part of the Joint Polar Satellite System (JPSS) program [30], launched in 2011. CrIS is in a sun-synchronous orbit, with mean local overpass times of 13:30 (ascending node) and 01:30 (descending node) [31–34]. CrIS has three bands in the infrared region (645–1095, 1210–1750, and 2155–2550 cm−1) with a 2200 km swath width and sets of three-by-three circular footprints, each approximately 14 km at the nadir [31–33]. The maximum sensitivity near the surface is typically ~1 ppbv [31].
We used daytime quality flag (less than 4), degrees-of-freedom-of-signal (less than or equal to 0.1) and χ2 measurements and removed low-quality data or outliers by applying the standard of (greater than or equal to 0.5).
These criteria were selected based on stronger correlation with Kangwha, on the western coast near the SMA.) with a range of 0.5 < R < 0.7.

## Slide 10: NH3 CrIs CFPR Spatiotemporal Patterns
NOAA Satellites Surface NH3 Measurements
(Shepard et al., 2020)
NOAA20
SNPP
Combined
Interpolated

## Slide 11: 2017 NEI NH3 Emissions from Agricultural Sector
Agricultural Sector: Fertilizer + Animals (Beef, Dairy, Swine, Broiler, Layers, Sheep, Horses, and Goats)

## Slide 12: 2017 NEI Ag NH3 Emissions by Animals & Fertilizer (Summer)
Beef
Broiler
Dairy
Layer
Swine
Fertilizer

## Slide 13: Performance of VAE-assimilation (2019)
CMAQ simulated
Annual mean surface NH3 concentration (2019)
VAE assimilated
Satellite retrieved

## Slide 14: Performance of VAE-assimilation (June 2019)
Blue: CMAQ Simulation
Red: VAE-assimilation
Black: CFPR Satellite

## Slide 15: NH3 Emissions Comparison (2019)
Important to utilize the spatial and temporal coverages from the CrIs NH3
Relatively underestimated NH3 from Beef vs overestimated NH3 from Swine
Indicating that the significant differences over the Great Plains and Southwest regions
Prior Emissions | Posterior Emissions

## Slide 16: Sector-level NH3 Emissions Comparison (2019)
Beef Cattle
Swine

## Slide 17: Findings
A significant amount of surface NH3 concentrations changes by location and time/dates
Requires a better spatiotemporal representation of NH3 from livestock wastes
DeepCTM/VAE performed well in capturing the spatial and temporal differences of NEI Livestock Waste NH3 against the observations
Identified the sector-level (anima-specific) NH3 differences for the calibrations of animal-specific NEI Emissions from the Farm Emissions Model used in NEI development
Swine and Beef Cattle shows the lack of spatiotemporal representations
  Swine: Overestimations of NH3 over the areas in Iowa and NC (most swine-dense area)
  Beef: Underestimation of NH3 over the areas in TX, KY, CO, NE, SD, ND, and MT, while the overestimation occurred over CA.
    Regional farm management practices input to the FEM need an update to address this issue.

## Slide 18: Thank you!
  ACKNOWLEDGEMENT
  NOAA Atmospheric Chemistry, Carbon Cycle and Climate (AC4) [Grant# NA21OAR4310225]
  USEPA
  Korea National Institute of Environment Research