## Slide 1
Quantifying Aircraft Emissions with Inverse Modeling: A Case Study at the Los Angeles International Airport
Gavendra Pandey and Saravanan Arunachalam
Institute for the Environment, University of North Carolina at Chapel Hill
22nd Annual
CMAS Conference
October 16-18, 2023

## Slide 2
Aircraft Dispersion Modelling (Background)
Aircraft emissions from an airport are a significant source of total emissions that have an impact on air quality in the airport vicinity (Arunachalam et al, 2011).
Aircraft activities at airports produce CO2 and H2O emissions that affect climate as well as other pollutants (NOx, SOx, and PM2.5) that impact local air quality (Woody et al, 2011; 2015; 2016, Stettler et al., 2011; Levy et al, 2012; Ashok et al, 2017).
Aircraft sources are unique due to the transient nature of the emissions from each source, as well as the buoyant exhaust.
These sources emit the pollutants in short bursts, especially during landing and takeoff operations (LTO) and it is difficult to quantify these short bursts of emissions and model the governing processes.
Added complexity occurs when
  when the airport is situated near a shoreline where meteorological conditions are far from being spatially uniform.

## Slide 3
Quantifying Aircraft Emissions with Inverse Modeling: A Case Study at the Los Angeles International Airport (LAX)
Motivation
  Airports need a dispersion modeling system that incorporates all physical and chemical processes related to LAQ (Local Air Quality) around airports
  For the LAX study, we have seen that current regulatory model AERMOD underpredicts daytime concentrations even during hours with high emissions
Known limitations in AERMOD (Arunachalam et al, 2017; ACRP Report 179)
  Identified issues related to:
    Source representation: area vs. volume vs. line
    Lack of plume rise for hot buoyant plumes
    Limited treatment of chemistry
    Time Scale – Sub-Hourly Approach
    Shoreline effects to account for marine boundary layer
Objective
  To quantify aircraft emissions at a large airport using inverse modeling approach and compare those with existing emissions estimates
(Pandey et al., Atmos. Environ. 2022)
(Pandey et al., 2023 (Under Review)
(Pandey et al., Atmos. Environ. 2023)

## Slide 4: Model Evaluation with LAWA Study Data
AERMOD is evaluated with
  SO2 measurements from LAWA study conducted during winter and summer of 2012 at the AQ, CN, CS, and CE monitors shown in the figure
SO2 concentrations in the vicinity of the airport are dominated by aircraft emissions (given fuel Sulfur content)
  using 2 sets of meteorology:
    Original Meteorology generated by AERMET and
    Modified Meteorology based on region-specific modifications of AERMET outputs
    Pandey et al, Atmos. Environ., 2022
      Winter (Jan 31 – Mar 13, 2012)
      Summer (Jul 18 – Aug 28, 2012)
      17 Locations: 4 “core”, 4 “satellite”, 9 “gradient”
      Over 400 compounds measured
LAWA: Los Angeles World Airports

## Slide 5: Emissions (Aircraft: AEDT, Non-Aircraft: LAX-AQSAS)
Comparison of hourly averaged aircraft and non-aircraft SO2 and NOX emissions during the winter and summer field studies.
Aircraft SO2 and NOx emissions close to 50% of non-aircraft emissions in both seasons during 7-19 hours.
AEDT: Aviation Environmental Design Tool
LAX-AQSAS: Los Angeles Airport - Air Quality and Source Apportionment Study

## Slide 6
Modified Meteorological Conditions in AERMOD
Modified Meteorology
Source: Google
to account for the formation of the internal boundary layer that is formed when stable air from the ocean flows onto the warmer land surface of the airport,
urban roughness effects on winds flowing from Los Angeles, east of the airport.

## Slide 7: Implementation of Plume Rise and Shoreline Meteorology Results
Ratio of Modeled/Measured mean concentrations improved with plume rise and modified met during early morning and late night (when the base model had poor performance) hourly bins
Modeled/Measured mean SO2 concentrations averaged over hourly bins at the four core sites (summer 2012)
Regulatory update to the EPA’s Guideline on Air Quality Models - Appendix W with updated AERMOD for aircraft exhaust modeling
(EPA tested code submission and plans to include in next AERMOD release by Nov 2023)
Default – AERMOD base model
Plume Rise – AERMOD with aircraft plume rise,
Shoreline – AERMOD with PR and modified met,
Neutral – Westerly wind daytime hours convert to neutral
Other issues for daytime underpredictions remain, and hence we are resorting to inversion to see if there is a problem with emissions locations/magnitudes.
Pandey et al., Atmos. Environ. 2022 and 2023
AERMOD model performance significantly improved after adding plume rise and met modify.

## Slide 8: Inverse Modeling
A reverse of the forward problem becomes more important if the concentration measurements are known at given positions and times, mathematically it is known as an inverse problem.
Inverse problems are dealt within a classical parametric estimation framework (Data Assimilation).
Sources
Receptors
Forward Modeling
Inverse Modeling
S2
S3
S4
S1
R
R
R
R
R
R
R
R
S - Source, R - Receptor

## Slide 9: Data Assimilation / Inverse Modeling
Reference: Lewis, J. M., Lakshmivarahan, S., Dhall, S., Dynamic Data Assimilation: A Least Square approach., Cambridge University Press.
  Concentration Measurements
  Source-Receptor Relationship
  Inversion Technique
  Data for Validation
Primary Requirements

## Slide 10: Classical Least Squares Formulation
For m sources, there will be total 3m unknowns, 2m will be locations, and m intensities.
For two point sources, source-receptor relationship is
Objective function is
For fixed x1 and x2 ,
Classical optimization will not work
A new technique is proposed
Reference: Singh et al., 2013. Inverse Modelling for Identification of Multiple-Point Releases from Atmospheric Concentration Measurements. BLM 146, 277–295.

## Slide 11: Classical Least Squares Formulation
Critical points lead to system of equations
The Hessian matrix of second order partial derivatives
If Hessian matrix will be positive definite, estimate of q1 and q2 ensure minimum of J.
Reference: Singh et al., 2013. Inverse Modelling for Identification of Multiple-Point Releases from Atmospheric Concentration Measurements. BLM 146, 277–295.

## Slide 12: Classical Least Squares Formulation
Formulation for multiple point sources
If Hessian matrix will be positive definite, estimate of qi ’s ensure minimum of J.
Minimize objective function
Critical points lead to system of equations Aq = b
Reference: Singh et al., 2013. Inverse Modelling for Identification of Multiple-Point Releases from Atmospheric Concentration Measurements. BLM 146, 277–295.

## Slide 13: Proposed Methodology
Reference: Singh et al., 2013. Inverse Modelling for Identification of Multiple-Point Releases from Atmospheric Concentration Measurements. BLM 146, 277–295.

## Slide 14: Proposed Methodology
Inverse modeling is performed for non-reactive tracer gases
Number of sources are assumed a priori
Vertical and temporal dimensions are not taken into account
Limitations
Reference: Singh et al., 2013. Inverse Modelling for Identification of Multiple-Point Releases from Atmospheric Concentration Measurements. BLM 146, 277–295.

## Slide 15: Implementation of proposed methodology at LAX airport
  SO2 concentration measurements,
  (from four LAX-AQSAS core sites 10 min averaged concentration, total 24 measurements in one hour)
  Source-Receptor Relationship,
  (Adjoint as Gaussian Plume Model (by rotating wind direction 180 degrees))
  Inversion Technique
  (Least Squares inversion methodology)
  Data for Validation
  (Emission locations/magnitudes data from AEDT)
Domain Size:
Discretized Domain:
Mesh Size:
AEDT: Aviation Environmental Design Tool
LAX-AQSAS: Los Angeles Airport - Air Quality and Source Apportionment Study

## Slide 16
Discussion
AERMOD doesn’t account for aircraft plume dynamics in area/volume source treatment
  Proposed plume rise formulation for aircraft emissions modeled with AERMOD
  Forward modeling results demonstrate improved model performance after incorporating plume rise and modified meteorology
  AERMOD underpredicts during daytime hours even after applying above modifications
Resort to inverse modeling to assess potential problem with emissions locations/magnitudes
  Use the adjoint of a standard Gaussian dispersion model and least squares as an inversion technique
  Use SO2 concentration measurements from the LAX-AQSAS for evaluation and comparison
  Quantify the aircraft emissions locations/magnitudes using this complex approach
  Ongoing work, and hope to share results soon

## Slide 17
Acknowledgements
This work was funded by the U.S. Federal Aviation Administration Office of Environment and Energy through ASCENT, the FAA Center of Excellence for Alternative Jet Fuels and the Environment, project 19 through FAA Award Number 13-C-AJFE-UNC under the supervision of Jeetendra Upadhyay. ASCENT (Aviation Sustainability Center) (http://ascent.aero) is a U.S. DOT-sponsored Center of Excellence.
We thank Jeetendra Upadhyay and Mohammed Majeed of the FAA for several helpful discussions.
The authors wish to gratefully acknowledge the Los Angeles World Authority (LAWA) and the U.S. DOT Volpe Center for providing datasets from the LAX AQSAS Study.
Opinions, findings, conclusions and recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of ASCENT sponsor organizations.

## Slide 18
References
Arunachalam, S., A. Valencia, M. Woody, M. Snyder, J. Huang, J. Weil, P. Soucacos and S. Webb (2017). Dispersion Modeling Guidance for Airports Addressing Local Air Quality Concerns. Transportation Research Board Airport Cooperative Research Program (ACRP) Research Report 179, Washington, D.C. Available from: http://nap.edu/24881.
Arunachalam S., Woody M., Baek B.H., Shankar U., Levy J.I. (2011) An Investigation of the Impacts of Aviation Emissions on Future Air Quality and Health. In: Steyn D., Trini Castelli S. (eds) Air Pollution Modeling and its Application XXI. NATO Science for Peace and Security Series C: Environmental Security. Springer, Dordrecht.
Ashok, A., Balakrishnan, H., Barrett, S. R. H., 2017. Reducing the air quality and CO2 climate impacts of taxi and take-off operations at airports. Transportation Research Part D 54, 287-303.
Lewis, J. M., Lakshmivarahan, S., Dhall, S., Dynamic Data Assimilation: A Least Square approach., Cambridge University Press.
Levy, J.I., Woody, M., Baek, B.H., Shankar, U., Arunachalam, S., 2012. Current and future particulate-matter-related mortality risks in the United States from aviation emissions during landing and takeoff. Risk Anal. 32 (2), 237-249.
Pandey, G., Venkatram, A., Arunachalam, S., 2022. Evaluating AERMOD with measurements from a major U.S. airport located on a shoreline. Atmos. Environ. 119506.
Pandey, G., Venkatram, A., Arunachalam, S., 2023. Accounting for plume rise of aircraft emissions in AERMOD. Atmos. Environ. 120106.
Singh, S.K., Sharan, M., Issartel, J.-P., 2013. Inverse Modelling for Identification of Multiple-Point Releases from Atmospheric Concentration Measurements. Boundary Layer Meteorol. 146, 277–295. https://doi.org/10.1007/s10546-012-9765-y.
Stettler, M., Eastham, S., Barrett, S., 2011. Air quality and public health impacts of UK airports. Part I Emiss. Atmos. Environ. 45 (31), 5415-5424.
Woody, M., Baek, B.H., Adelman, Z., Omary, M., Lam, Y.F., West, J.J., Arunachalam, S., 2011. An assessment of aviations contribution to current and future fine particulate matter in the United States. Atmos. Environ. 45 (20), 3424-3433.
Woody, M.,West, J., Jathar, S., Robinson, A., Arunachalam, S., 2015. Estimates of nontraditional secondary organic aerosols from aircraft SVOC and IVOC emissions using CMAQ. Atmos. Chem. Phys. 15 (12), 6929-6942.