## Slide 1: Deep Learning based Digital Twin for Simulating CMAQ surface NO2 Levels over the CONUS Ahmed K. Salman, Yunsoo Choi, Jincheol Park, Seyedali Mousavinezhad, Mahsa Payami, Mahmoudreza Momeni, Masoud Ghahremanloo University of Houston

## Slide 2: Introduction to Digital Twin
Objective of Digital Twin is to simulate CMAQ NO2 concentration across CONUS
Accelerate simulation of CMAQ NO2 surface concentration
Derive emission sensitivities from Digital Twin in order of CMAQ DDM
Accelerate Inverse modeling of emission inventory

## Slide 3: Sub-set of CMAQ Input for Digital Twin
Category | Abbreviation | Variable name | Unit
SMOKE | NO | Nitric oxide emission | moles/s
SMOKE | NO2 | Nitrogen dioxide emission | moles/s
SMOKE | HONO | Nitrous acid emission | moles/s
SMOKE | VOC_INV | Total volatile organic compounds emission | moles/s
MCIP | PRSFC | Surface pressure | pascal
MCIP | TEMP2 | 2-m Temperature | K
MCIP | WSPD10 | 10-m wind speed | m/s
MCIP | WDIR10 | 10-m wind direction | degrees
MCIP | RGRND | Solar radiation reaching the surface | watts/m2
MCIP | Q2 | Mixing ratio At 2-m | kg/kg
MCIP | PBL | Planetary boundary level height | m
MCIP | RN | Nonconvective Pcpn per Met Tstep | cm
MCIP | RC | Convective Pcpn Per Met Tstep | cm
LULC | HGT_M | Terrain elevation | m
LULC | URBANDEV | Urban development | -
LULC | ALBEDO12M | Surface albedo | -
LULC | GREENFRAC | Green fraction | -
LULC | LANDMASK | Land-water mask | -
Total 18 channels of inputs are fed to Digital Twin

## Slide 4: Digital Twin grid-discretization
Spatial resolution: 12 km Temporal resolution: 1 hour
Discretized CONUS grid into 768 x 768 km2 sub-grids
Addresses GPU memory allocation issue while training Digital Twin
Augments the training data and prevents model overfitting

## Slide 5: Digital Twin U-Net architecture
Train period: Summer 2011 & 2014
Test period: Summer 2017

## Slide 6
Digital Twin 3-fold monthly cross-validation (NO2 estimation)
Train period (2011, 2014, 2017) | Test period (2011, 2014, 2017) | Correlation | IOA | MAE (ppb) | SMAE
July & August | June | 0.979 | 0.989 | 0.22 | 0.151
June & August | July | 0.981 | 0.99 | 0.214 | 0.147
June & July | August | 0.978 | 0.988 | 0.22 | 0.151
 |  | 0.979 | 0.989 | 0.218 | 0.15
Digital Twin performance on our Test-case
Train period (Summer) | Test period (Summer) | Correlation | IOA | MAE (ppb) | SMAE
2011 & 2014 | 2017 | 0.949 | 0.974 | 0.228 | 0.211
Performance of model is higher when test period is closer to the training period
Evaluating model on a test dataset with a gap of 3 years is challenging (data shift)

## Slide 7: Sample Digital Twin estimation across US

## Slide 8: Sample Digital Twin estimation across US

## Slide 9: Sample Hourly NO2 time-series

## Slide 10: Digital Twin Monthly Performance
2017 | CMAQ STD (ppb) | Mean Bias (ppb) | MAE (ppb) | NMAE
June | 1.651 | 0.029 | 0.218 | 0.214
July | 1.643 | 0.018 | 0.22 | 0.205
August | 1.816 | 0.01 | 0.245 | 0.214
NO2 conc. reduced from 2011 to 2017
Digital Twin generally overestimates, inherited bias from training data
MAE in August is relatively higher due to higher variance in NO2 conc.

## Slide 12
Taylor Diagram of Simulated Hourly NO2 Spatially Averaged across Cities

## Slide 14: NOx emissions to NO­2 concentration sensitivity
Derived semi-normalized NOx sensitivity using the Mass Balance approach
NO2 concentration
NOx emissions
Initial sensitivity coefficient
Compared Digital Twin based sensitivity with CMAQ DDM for validation

## Slide 15: Monthly average sensitivity comparison

## Slide 17: Computational Performance
1-hour NO2 simulation over CMAQ-US grid
Model | Resources | Compute Time
CMAQ | 1 CPU | 71.75 (mins)
CMAQ | 28 CPUs | 4.08 (mins)
Digital Twin | 1 CPU | 10.5 (sec)
Digital Twin | 28 CPUs | 3.71 (sec)
Digital Twin | 1 GPU, 1 CPU | 6.83 (sec)
Digital Twin | 1 GPU, 28 CPUs | 2.15 (sec)
With 1 CPU, Digital Twin is more than 400 times faster than CMAQ
With 1 CPU and 1 GPU, Digital Twin is more than 600 times faster than CMAQ
Efficient programming and multi-GPU processing can further reduce computational time
CPU: Intel(R) Xeon(R) Gold 6252; GPU: NVIDIA A30 (24 GB)

## Slide 18: Future direction
Use PCNN to impute missing observation data across CONUS
Apply iterative Finite Difference Mass Balance (iFDMB) approach on Digital Twin to update emission inventory across CONUS
Feed optimized emission inventory to CMAQ to improve NO2 concentration accuracy

## Slide 19: Acknowldgements
NASA's Aura Science Team Grant (NNH19ZDA001N-AURAST).
UH high research priority funding