## Slide 1: Machine Learning with Spatial Interpolation Techniques for Constructing 2D Ozone Concentrations in Southern California during the COVID-19 Shutdown
Khanh Do1,3, Arash Kashfi Yeganeh1, Ziqi Gao2,
Yang Zhang3, and Cesunica E. Ivey1,4
22nd CMAS Conference, Chapel Hill, NC, October 17, 2023
1Department of Chemical and Environmental Engineering, University of California, Riverside, CA
2Department of Civil and Environmental Engineering, Georgia Institute of Technology, Atlanta, GA, USA
3Department of Civil and Environmental Engineering, Northeastern University, Boston, MA
4Department of Civil and Environmental Engineering, University of California, Berkeley, CA
Notes: 14’

## Slide 2
Objectives
  Evaluate the deterministic and machine learning (ML) models under rapid changes in emissions and meteorology
  Investigate ozone (O3) concentrations during the lockdown
Why ML and what’s new?
  Increase computational efficiency
  Fill the sparse air monitoring network
  Investigate if the pattern that have occurred in the past
  Enable the use of historical data for prediction anywhere with the hybrid model (ML + spatial interpolation)
Notes: 1:45’

## Slide 3
25 years of historical data of mean annual NOx
O3 design values for the South Coast
Significant NOx decrease as a result of the emissions control programs implemented
The 8-hour O3 design value for SoCAB marginally increased since 2014
What caused O3 increase in recent years?
NOx and O3 Trends in Southern California
Notes: 2:27’

## Slide 4
Machine Learning Methods
ML model
  Step 1: use Random Forest Regression (RFR) to predict O3 concentrations at 15 air monitoring sites
  Step 2: apply three different spatial interpolation methods (ordinary kriging, inverse distance weighting (IDW), and bicubic interpolation)
  Step 3: evaluate interpolated results with 12 additional sites
ML model training
  Training features: NO2, NO, temperature (T), relative humidity (RH), wind speed (WS), wind direction (WD), O3
  Training year: 2009, 2010, 2016, 2017, 2019; and evaluation year: 2020
  Prediction at 15 sites using ML, and a 2-D O3 data constructed using interpolation
Notes: 5:21’

## Slide 5
IWD
Consider distances between interpolating points
Have more significant influence from neighbor points
Ordinary Kriging
Consider distances between interpolating points
Predict the optimum value by linear combining the known values and its weight , variogram
Bicubic Interpolation
Based on third-degree polynomial
Data interpolate on a rectangular grid with even distribution
Interpolation Methods
Notes: 5:55’

## Slide 6: Snapshots of Interpolation
Kriging interpolation captures the O3 trend in Southern California
  Low O3 levels observed in the southwest
  High O3 levels in Inland Empire
All interpolation methods perform well in low O3 regions
Bicubic and IDW struggle to capture high O3 regions
2-D hourly O3 (16:00 on 06/22/2020). Evaluation sites: dots with white borders; ML sites: dots without borders
Notes: 6:43’

## Slide 7: Temporal Evaluation (hourly)
The map shows 27 air monitoring sites in the SoCAB
All three methods capture the O3 trends in Southern California
They underestimate the peaks due to ensemble learning from RFR
Pomona
Notes: 7:48’

## Slide 8: Temporal Evaluation (monthly)
Monthly mean bias computed at 15 sites for 2020. The kriging interpolation method: dash lines; CMAQ simulation: solid lines
MB for kriging interpolation centering around zero
CMAQ simulation overestimated the ozone levels
Seasonal variation has not well represented in CMAQ
O3 concentrations in the SoCAB
  Highest during the summer
  Lowest in the winter
Poor CMAQ results could come from the emissions
Notes: 8:38’

## Slide 9: Statistical Evaluation
Daily average R2 values of 2020 were evaluated at 6 selected sites
Bicubic R2 indicates the poorest performance among the three methods
IDW shows a significant improvement from bicubic interpolation
  IDW accounts for the distances between the interpolation points and the data points
Kriging results in the best interpolation method
  Accounts for the distance
  Considers the variability of data by computing the variance
CMAQ has poor predictions at Los Angeles International Airport (LAX) and Crestline locations
  LAX is situated near the the Pacific Ocean
  Crestline is 1406 meters above sea level
Sites | Bicubic | IDW | Kriging | CMAQ
LAX | 0.31 | 0.48 | 0.65 | 0.25
Glendora | 0.46 | 0.53 | 0.72 | 0.52
Lake Elsinore | 0.52 | 0.70 | 0.79 | 0.56
San Gabriel | 0.53 | 0.77 | 0.81 | 0.62
Rubidoux | 0.46 | 0.65 | 0.86 | 0.68
Fontana | 0.88 | 0.89 | 0.87 | 0.59
Notes: 9:44’

## Slide 10: ML Performance during the Lockdown
a
b
Lake Elsinore
  ML captures the O3 trends throughout the periods
  Lake Elsinore is in a remote area
  The results indicate NOx-limited regime
Fontana
  ML does not capture O3 trends during the lockdown
  Fontana is an urban site
  The results indicate VOC-limited regime
c
d
O3 Diurnal Profile
Pre-lockdown
During the Lockdown
Notes: 12:07’

## Slide 11
AQMs and ML models serve different purposes
ML with spatial interpolation
  Offer a fast and cost-effective approach for sensitivity tests
  Focus only for one species
  Require quality of data and relevant features
  Predict based on historical data
AQMs
  Project future O3 predictions in response to emission controls
  Enable greater spatial resolution
  Provide simulation data over a large domain
  Simulate multiple air pollutant species
ML or Air Quality Models?
Notes: 14:09’

## Slide 12
The ML model performs well before and after the lockdown
The ML model struggles to predict O3 concentrations during the lockdown
  There is not a similar pattern in air quality during the lockdown
  Train the model with VOC data will improve the results
Policy implications
  Fast visualization about NOx- and VOC-limited regimes
  Effective control strategies for emission reductions
  Complement and support regulatory AQMs
Conclusions
Notes: 15:15’

## Slide 13
South Coast Air Quality Management District (SCAQMD)
Dr. Armistead G. Russell for supporting the project
Dr. Sang-Mi Lee for supervising the project
Graduate Assistant in Areas of Need (GAANN)
Acknowledgments

## Slide 14: Backup slides

## Slide 15
Methods
2-D ozone concentrations
  Step 1: used Random Forest Regression (RFR) to predict ozone concentrations at each air monitoring location (15 sites)
  Step 2: applied three different spatial interpolation methods (ordinary kriging, inverse distance weighting (IDW), and bicubic interpolation)
  Step 3: evaluated interpolated results with 12 additional sites
Figure 3. Data from 15 air monitoring stations (Anaheim, Azusa, Banning, Compton, Fontana, Glendora, Lake Elsinore, LAX, LA North Main Street, Mira Loma, Rubidoux, San Gabriel, Santa Clarita, San Bernardino, Upland) were used for ML model predictions of ozone concentrations.
Figure 4. Three node decision trees based on air quality and meteorological input. The meteorology data is from LAX, and air quality data is from Fontana. The predictions were made based on 12:00 noon to 5:00 PM training data.
Conclusion
Background/
Objective
Results
Methods

## Slide 16
Methods
CMAQ Configurations
  North American Mesoscale Forecast System (NAM) with high-resolution SST
  4km resolution
  2020 emissions were carried out with two-step corrections
    2020 emissions were obtained based on 2019 emissions with the AQMD emission projection
    Correction for traffic reduction due to the pandemic lockdown based on weekly traffic change in 2020 provided from the UCR emission group from Jan 1st to Sep 30th of 2020. Using 2991 observed traffic locations in Southern California to interpolate the emission profiles.
Figure 5: The finest domain (blue lines) with 4 km horizontal resolution covered the entire SCAQMD region (thick black lines).
Conclusion
Background/
Objective
Results
Methods

## Slide 17: Results and Model Evaluation
Building Sites
Evaluating Sites
Evaluation metrics
  15 building sites and 12 evaluation sites
Model performance increases from the West to the East
  Predict poorly for Crestline site
LAX is not a function of meteorology
M.B. indicates
  Overestimating the building sites
  Underestimating the evaluation sites
Evaluation Sites | C.C. | M.B. | R.M.S.E.
Crestline | 0.64 | -0.0122 | 0.020
La Habra | 0.87 | 0.0033 | 0.008
Long Beach | 0.75 | -0.0006 | 0.009
Mission Viejo | 0.69 | -0.0040 | 0.011
North Hollywood | 0.88 | 0.0003 | 0.009
Pasadena | 0.88 | -0.0016 | 0.009
Perris | 0.89 | 0.0031 | 0.009
Pomona | 0.91 | 0.0020 | 0.009
Redlands | 0.84 | -0.0070 | 0.013
Reseda | 0.84 | -0.0042 | 0.011
West LA | 0.77 | 0.0022 | 0.009
Winchester | 0.62 | -0.0051 | 0.013
Building Sites | C.C. | M.B. | R.M.S.E.
Anaheim | 0.85 | 0.0025 | 0.008
Azusa | 0.87 | 0.0007 | 0.009
Banning | 0.85 | -0.0018 | 0.009
Compton | 0.87 | 0.0053 | 0.008
Fontana | 0.93 | 0.0011 | 0.007
Glendora | 0.84 | -0.0045 | 0.010
Lake Elsinore | 0.89 | 0.0002 | 0.007
LAX | 0.80 | 0.0033 | 0.008
LA North Main | 0.88 | 0.0031 | 0.008
Mira Loma | 0.92 | 0.0000 | 0.008
Rubidoux | 0.92 | 0.0014 | 0.007
San Gabriel | 0.89 | 0.0022 | 0.008
Santa Clarita | 0.91 | 0.0003 | 0.008
San Bernardino | 0.92 | 0.0010 | 0.009
Upland | 0.92 | -0.0003 | 0.008
Figure 10: Scatter plots for building sites
Figure 11: Scatter plots for evaluation sites
Table 2: Evaluation metrics for 15 building sites.
Table 1: Evaluation metrics for 12 evaluation sites.
Notes: To evaluate the model, we computed different evaluation metrics for 15 building sites and 12 evaluation sites. Figure 6 and 7 are scatter plots plotting the predicted ozone concentrations and observation for 4 different locations resulting the high r-square and the slops are closed to 1.
The model performance increases from the West to the East and predicted poorly for Crestline site. Ozone at LAX is not a function of meteorology. From the mean bias, the model was overestimating the ozone concentration for the building sites and underestimating for the evaluation sites.

## Slide 18
2-D interpolation reduced simulation time and provided a high-resolution details of air pollution maps
Cubic interpolation captured extreme peaks of ozone
IDW is localized, significantly influenced by the nearest neighbors
Kriging has better overall performance from statistical benchmark
ML is more consistent than CMAQ
  Provide accurate results over the entire simulation period
  Capture air quality trends
Results and Model Evaluation
Figure 14: Hourly ozone heatmap (@16pm June 22, 2020) using kriging interpolation
La Habra
Anaheim
WLA VA
Riverside
La Habra
Anaheim
WLA VA
Riverside
La Habra
Anaheim
WLA VA
Riverside
Figure 12: Time series plotting ozone concentrations for CMAQ model, cubic interpolation, and observation
Figure 13: Time series plotting ozone concentrations for three different interpolation methods (kriging, cubic, and IDW) with observation
Figure 15: Hourly ozone heatmap (@16pm June 22, 2020) using cubic interpolation
Figure 16: Hourly ozone heatmap (@16pm June 22, 2020) using IDW interpolation
Notes: This slide compares different interpolation methods. Figure 7 is the time series plotting the ozone concentrations for CMAQ (orange line), cubic interpolation (black marker), and observation (blue line). By observation, cubic interpolation performed better. Figure 7 comparing three different interpolation methods, kriging, cubic, and IDW.
Figure 9, 10, 11 show the heatmap generated by interpolation. Cubic was able to capture the extreme peaks of air pollution. IDW is localized and significantly influenced by the nearest neighbors. Kriging has better overall performance from statistical benchmark.

## Slide 19: Statistical evaluation
Sites | Bicubic | IDW | Kriging | CMAQ
Anaheim | 0.66 | 0.67 | 0.74 | 0.41
Azusa | 0.52 | 0.64 | 0.77 | 0.59
Banning | 0.17 | 0.46 | 0.73 | 0.26
Compton | 0.65 | 0.67 | 0.77 | 0.48
Fontana | 0.88 | 0.89 | 0.87 | 0.59
Glendora | 0.46 | 0.53 | 0.72 | 0.52
Lake Elsinore | 0.52 | 0.70 | 0.79 | 0.56
LA North Main ST | 0.36 | 0.67 | 0.78 | 0.48
LAX | 0.31 | 0.48 | 0.65 | 0.25
Mira Loma | 0.56 | 0.71 | 0.86 | 0.67
Rubidoux | 0.46 | 0.65 | 0.86 | 0.68
San Bernardino | 0.68 | 0.85 | 0.86 | 0.67
San Gabriel | 0.53 | 0.77 | 0.81 | 0.62
Santa Clarita | 0.27 | 0.72 | 0.84 | 0.61
Upland | 0.76 | 0.80 | 0.86 | 0.61
Daily average R2 values of 2020 were evaluated at 15 sites used for interpolation points for three interpolation methods. The R2 for CMAQ was computed using the five highest ozone months from May to September 2020.
Bicubic R2 indicates the poorest performance between the three interpolation methods
IDW shows a significant improvement from bicubic interpolation. Since IDW accounts for the distances between the interpolation points and the data points
Kriging resulted in the best interpolation method. Kriging accounts for the distance and considers the variability of data by computing the variance.
CMAQ gave poor predictions on LAX and Crestline locations. LAX is influenced by the Pacific Ocean and Crestline is 1406 meters above sea level.

## Slide 20: Results
Averaged diurnal profiles of 2016 - 2019 (blue), actual 2020 (red), and ML predicted 2020 (black) ozone concentrations (ppm) at Lake Elsinore for three different periods: (a) pre-lockdown (Jan to Feb), (b) lockdown (Mar to May), and (c) post-lockdown (after May). The shaded area is the standard deviation of the 2016 - 2019 measurements.
a
b
c
Ozone concentrations at Lake Elsinore were lower during the lockdown and back to normal after the lockdown
ML captured the ozone trends throughout the periods
Lake Elsinore is from remote area
The results indicate NOx limited regime
Conclusion
Background/
Objective
Results
Methods

## Slide 21: Results
Averaged diurnal profiles of 2016 - 2019 (blue), actual 2020 (red), and ML predicted 2020 (black) ozone concentrations (ppm) at Fontana for three different periods: (a) pre-lockdown (Jan to Feb), (b) lockdown (Mar to May), and (c) post-lockdown (after May). The shaded area is the standard deviation of the 2016 - 2019 measurements.
a
b
c
Ozone concentrations at Fontana were higher during the lockdown and did not back to normal after the lockdown
ML did not capture the ozone trends during and after the lockdown periods
Fontana site is an urban site
The results indicate VOC limited regime
Conclusion
Background/
Objective
Results
Methods

## Slide 22: Effects of Meteorology
Fontana ozone trends for 90th (black), 98th (blue) percentile, and annual average (orange). The dash lines were predicted with hourly average temperature and RH from 1994 to 2018. The solid lines were predicted with actual values. (Do et al., Environmental Science: Atmospheres, Under Revision)
ML model easily predicts changes of the target (ozone) label with a perturbation of input features
Minimizing the effects of heat waves or foggy days by averaging T and RH from 1994 to 2018
Adjusted line shows a strong downward ozone trend from 1994 to 2010 but resisting further decrease
Meteorology has a minor effect on the annual average

## Slide 23
Machine learning methods
NO2, NO, temperature, RH, wind speed, wind direction, ozone
Training years from 2009 – 2019 and evaluating year is 2020
15 sites were predicted using ML, and a 2-D ozone heat map was constructed using interpolation based on 15 ML sites
Training sites | Anaheim, Azusa, Banning, Compton, Fontana, Glendora, Lake Elsinore, LAX, LA North Main Street, Mira Loma, Rubidoux, San Gabriel, Santa Clarita, San Bernardino, Upland
Features | NO2, NO, temperature, relative humidity, wind speed, wind direction
Label | Ozone
Data sources | EPA AQS data mart, CARB AQMIS
Training years | 2009, 2010, 2016, 2017, 2018, 2019
Evaluation year | 2020
Data summary for machine learning modeling