## Slide 1: The Well-tempered deposition algorithm
Colin Lee*1, Paul Makar 1, Kenjiro Toyota 1, Christian Hogrefe2, Olivia Clifton3,4, Mhairi Coyle5, Erick Fredj6, Orestis Gazetas7,8, Ignacio Goded7, László Horváth9, Qian Li10, Ivan Mammarella11, Giovanni Manca7, J. William Munger12, Ralf Staebler1, Eran Tas10, Timo Vesala11,13, Tamás Weidinger14, Zhiyong Wu15, Leiming Zhang1
Oct 17
CMAS 2023
1 Air Quality Research Division, Environment and Climate Change Canada
2 United States Environmental Protection Agency, Office of Research and Development
3 NASA Goddard Institute for Space Studies
4 Center for Climate Systems Research, Columbia Climate School, Columbia University
5 United Kingdom Centre for Ecology and Hydrology
6 Department of Computer Science, The Jerusalem College of Technology
7 European Commission, Joint Research Centre (JRC)
8 Scottish Universities Environmental Research Centre (SUERC)
9 Department of Optics and Quantum Electronics, ELKH-SZTE Photoacoustic Research Group
10 The Institute of Environmental Sciences, The Robert H. Smith Faculty of Agriculture, Food and Environment, The Hebrew University of Jerusalem
11 Institute for Atmospheric and Earth System Research/Physics, University of Helsinki
12 School of Engineering and Applied Sciences and Department of Earth and Planetary Sciences, Harvard University
13 Institute for Atmospheric and Earth System Research/Forest Sciences, University of Helsinki
14 Department of Meteorology, Institute of Geography and Earth Sciences, Eötvös Loránd University
15 ORISE Fellow at Center for Environmental Measurement and Modeling

## Slide 2: Ozone dry deposition
Ozone dry deposition is an important driver of ozone concentrations
Most implementations based on Wesely 1989
  Including in ECCC’s coupled weather and air quality model, the Global Environmental Multiscale—Modelling Air Quality and Chemistry (GEM-MACH)
Long-term deposition observations* are rare
  Require tower measurements for gradient (several heights) or eddy flux (high-time resolution concentration + vertical wind)

## Slide 3: AQMEII4 o3 tower site data
8 sites with tower measurements covering 5 land types over 3-12 years with ~35 met variables

## Slide 4: Machine learning is popular
Recent developments in machine learning (ML) and artificial intelligence (AI) have created an explosion of applications
This dataset is a great candidate for ML
  Many input variables (~30 common to all sites)
  Almost 100,000 valid observations in total
Number one fear: machine learning is “not interpretable”
  Especially deep neural networks
Great recent work on “explainable AI”
Another approach: Physics-Informed AI
  Build physical constraints into your model or loss function

## Slide 5: Goal: physics informed deep resistance model
Most deposition algorithms use “resistance model” with different deposition pathways represented as resistors in parallel or in series
Can we use the input variables related to each pathway to train a neural network (NN) to predict the resistance components and then add these up in parallel?

## Slide 6: How well does our physical model do?
Comparing GEM-MACH implementation against observations:
R
RMSE
Observed Vd (m/s)
GEM-MACH Vd (m/s)

## Slide 7: Detour: abusing tensorflow
TensorFlow is a mature and powerful machine learning platform in Python
  TensorFlow operations are differentiable
  TensorFlow has built-in optimisation routines
Part of the physics-informed NN development process involved translating the Fortran dry deposition code into TensorFlow operations
I was therefore able to use TensorFlow to optimise the tunable parameters in our implementation of the Wesely scheme
This is not recommended, I mostly did it to see what would happen

## Slide 8: Tensorflow-tuned parameters
Comparing GEM-MACH algorithm with parameters tuned to observations
R
RMSE
Some improvement over baseline, but not huge
Observed Vd (m/s)
GEM-MACH Vd (m/s)

## Slide 9: Question 1: is there enough information?
Method: train traditional fully-connected neural network (black box) on all the observational data
Result: R
RMSE
Bias
There is information here!
But this is still a black box
On to physics-informed NN
Observed Vd (m/s)
Neural Network Vd (m/s)

## Slide 10: Physics informed network setup
Structure:
  3 neural networks for diffusion, aerodynamic and surface resistance terms
  Each takes only the inputs our physical algorithm uses, e.g. rdiff only uses friction velocity, no other inputs
  Output:

## Slide 11: Physics-informed results
Result: R
RMSE
Bias
Almost as good as the black box, except now we have information about what the model is “thinking”
Observed Vd (m/s)
Neural Network Vd (m/s)

## Slide 12: Conclusions and future work
We can use the physics-informed model to learn improve the physical model
  E.g., can easily change which variables go into each resistance
Physics-informed model can be taken further: break surface resistance down into soil, canopy, stomatal components instead of one large network
Test it out in regional model
  I expect it to fail spectacularly, but we will learn a lot
  How do we handle un-represented land types?
The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA.