## Slide 1: Pile Burning Estimates in the 2022 Emissions Modeling Platform
James Beidler 1, Jeff Vukovich 2, George Pouliot 1, Venkatesh Rao 2
1 Office of Research and Design, US EPA; 2 Office of Air and Radiation, US EPA
2024 CMAS Conference, Chapel Hill, NC
Source: https://forestry.nv.gov/uploads/hero-backgrounds/Spooner_Rx_Burn_-_202220220115_0021.JPG

## Slide 2: What is a Pile Burn?
Piles in Rocky Mountain National Park
Image source: https://www.nps.gov/subjects/fire/images/12_co_romo_FireAdaptedCommunities.jpg
Thinned or downed woody
biomass are placed into piles
Piles may sit until wood is dry and conditions are right for ignition
Piles can be stacked by hand or machine in a variety of geometries and sizes

## Slide 3: Why are pile burns important?
Source: Oregon Department of Forestry 2022 Oregon Smoke Management Report
~75-90% of area treated with fire in Oregon each year are in the form of pile burns.
Pile burn (PB) emissions estimates not included in 2020 NEI methods
Rx Fire a large contributor to PM in CONUS
2020 NEI misclassed pile burns as area prescribed burns (e.g. broadcast and underburn)

## Slide 4: Land Manager Tools for Pile Burn Emissions
The US Forest Service (USFS) and University of Washington (UW) maintains a pile burn calculator based on methods in CONSUME and Hardy 1996.
https://depts.washington.edu/nwfire/piles/

## Slide 5: Estimating Pile Burn Emissions
Pile Burning Emissions = Biomass Burned * Emission Factor
Biomass burned (tons) =
  (All calculations are equivalent)
  or
  or
  or
Emission factors (g/kg)
  Smoke Emissions Reference Application (SERA) pile burn factors
  By combustion phase where possible: flaming vs. smoldering vs. residual

## Slide 6: Estimating Biomass Burned From Activity
Activity supplied as a mass
  If it is burned or consumed – great! Nothing more to do.
  If it is total mass in pile – apply the consumption fraction (75-95% Hardy 1996) (90-95% Wright 2019)
Activity supplied as a pile volume
  Determine packing ratio to calculate effective volume (0.1-0.3 Hardy 1996/CONSUME v3) for machine piles
  Determine wood species to calculate mass using biomass density (Miles 2009) or regression formula (Wright 2010)
Activity supplied as a geometry
  Determine best volume formula to calculate pile volume
  Follow the pile volume method above
Image source: Hardy 1996

## Slide 7: Estimating Biomass Burned from Area
4.5 tons/acre median value derived from CA and WA permit data
Em
For states and agencies that only provide area:
Em

## Slide 8: 2022 Pile Burn Activity
Chart: 2022 Pile Burn Records by State
| AK | AZ | AR | CA | CO | FL | ID | IN | IA | MD | MI | MN | MT | NE | NV | NM | ND | OK | OR | SD | UT | WA | WI | WY
Pile Burns | 8 | 260 | 30 | 3221 | 280 | 3534 | 399 | 1 | 6 | 9 | 23 | 33 | 889 | 2 | 99 | 14 | 4 | 5 | 4163 | 48 | 121 | 2671 | 3 | 510
EPA received pile burn activity from
  13 States
  2 Federal Agencies
  1 Tribe
Permit and other activity critical to emissions estimates
Each record may represent multiple piles

## Slide 9: 2022 Pile Burn Workflow
Non-ag and grassland satellite detects
ICS-209(WF)
WFIGS (WF)
FACTS(WF/Rx/PB)
DOI (Rx/PB)
Python Modified SmartFire2
Day-specific Fire lat-lon, Type and Acres Burned
State/Local/Tribe (Rx and PB)
BlueSky
Pipeline
Pile Burn
Processor
PB
WF/Rx
Pile Burn (PB) activity removed from wildfire (WF) and prescribed fire (Rx) workflow
8% of PB permits reconcile spatially and temporally with satellite fire detections (HMS)
Pile Burn Emissions

## Slide 10: 2022 National PM2.5 for All Wildland Fires
Chart: 2022 Western US Wildland Burning PM2.5 (tons) by Type
Chart: 2022 National Wildland Burning PM2.5 (tons) by Type
| RX | WF | PB
PM2.5 tons | 1086420.0308 | 938363.3493 | 16087.5474
Chart: 2022 West Coast Wildland Burning PM2.5 (tons) by Type
| RX | WF | PB
PM2.5 tons | 58541.7101 | 408973.9952 | 11681.9733

## Slide 11: 2022 Pile Burn PM2.5 By County

## Slide 12: Impact on PM2.5: PB vs Broadcast Rx
2022 USFS FACTS Pile Burn Activity Associated with HMS Detects
Broadcast Rx Processed through BlueSky as Rx Area Burns
PB Processed as piles using the draft pile burn method
Area treated is equivalent between methods
86% Reduction in PM2.5
Chart: 2022 FACTS Prescribed Fire Consumption
| AZ | CA | CO | ID | MT | NM | ND | OR | SD | UT | WA | WY
Consumption as a Broadcast Rx (tons) | 11825 | 88808 | 41109 | 33583 | 32069 | 9586 | 282 | 122329 | 7194 | 12870 | 99434 | 21016
Consumption as a Pile Burn (tons) | 10223 | 28554 | 5493 | 10815 | 11583 | 5514 | 180 | 52954 | 2443 | 4594 | 22256 | 6065
Chart: 2022 FACTS Prescribed Fire PM2.5
| AZ | CA | CO | ID | MT | NM | ND | OR | SD | UT | WA | WY
PM2.5 as a Broadcast Rx (tons) | 229 | 1917 | 1015 | 676 | 612 | 189 | 6 | 2481 | 150 | 185 | 2045 | 396
PM2.5 as a Pile Burn (tons) | 88 | 245 | 47 | 93 | 99 | 47 | 2 | 453 | 21 | 39 | 191 | 52

## Slide 13: Conclusions
PM emitted per acre burned is ~85% lower when modeled as a pile burn instead of a broadcast burn for detected fires
  Suggests historical overestimates of emissions from Rx fires in 2020NEI if treated area is equivalent
  Permit data is largely in excess of what was previously detected by satellites, resulting in PM increases for some areas
It all starts with activity: state/local/tribal permit data is crucial
Pile burn practices vary resulting in large tons/acre differences

## Slide 14: Modeling and Future Work for 2023 NEI
Temporal factors by combustion phase if possible, currently using broadcast burn profiles
  Pile burns may occur over snow and can have long smoldering tails
Plume rise method – heat output from a single representative pile
  Estimates using SMOKE/CMAQ Briggs approach show most in lowest layers
HAPs and pile-specific speciation profiles
Pile Burns included in 2023 NEI request for data

## Slide 15
Contact: James Beidler Beidler.James@epa.gov
The views expressed in this presentation are those of the author(s) and do not necessarily represent the views or the policies of the U.S. Environmental Protection Agency.
https://forestry.nv.gov/uploads/missions/Spooner_Rx_Burn_-_202220220220_0012.JPG