## Slide 1: Recent Gaseous and Particulate Emission Trends in Northeast Asia Using Top-Down Emission Adjustment Method with Surface Observations
Seongeun Jeong, Eunhye kim, Yoon-Hee Kang, Soontae Kim
Ajou University, South Korea
CMAS Conference 2024
October 23, 2024

## Slide 2
Motivation: Air Quality Overview in Northeast Asia
In Northeast Asia, air quality has long been recognized as poor, leading to ongoing studies focused on improvement.
Understanding the source-receptor relationship between upwind and downwind regions is crucial because northwesterly winds are predominant in winter.
Chart: Annual PM2.5 concentrations in 2023
| South Korea | French | UK | US
 | 20 | 10 | 8 | 14.3
--- South Korea annual average air quality standards : 15 μg/m3
--- WHO annual average air quality guidelines : 5 μg/m3

## Slide 3
Motivation: International Projects Focused on Upwind-Downwind Relationship
Many international projects have been carried out to enhance understanding of upwind and downwind impacts.
https://espo.nasa.gov/asia-aq/category/Mission/ASIA-AQ
2016
Beijing
https://www.sijaq.org/
2024

## Slide 4
Motivation: Determining Factors of PM2.5 Levels in South Korea
PM2.5 concentrations in South Korea are significantly influenced by both foreign and domestic emissions (left figure).
Ensuring simulation accuracy from the upwind region is crucial.
< South Korea>
Foreign + Domestic
PM2.5
Domestic
Foreign
PM2.5 Concentrations in South Korea.

## Slide 5
Motivation: Air Quality Overview in Northeast Asia
Previous studies reported that rapid changes in emissions in China have led to improvements in air pollution concentrations.
Capturing these changes in China, as the upwind source for South Korea, is crucial for accurately forecasting or estimating health impacts in South Korea
Beijing
Gu et al., (2023)
Shah et al., (2020)
Rapid changes in emissions

## Slide 6
Characteristics of Bottom-Up Inventories
Differences in Air Pollution Forecast Concentrations and Domestic and Foreign contributions
Bottom-up Emission Inventory
Choi et al. (2018)
Forecasting
Policy effects
Kang et al. (2022)
The available emission inventory (EI) in South Korea is based on data from the year 2021.

## Slide 7
The Need for Top-Down Emission Approaches
Various previous studies have proposed methods for adjusting emissions using satellite observations and ground-based measurement data.
Xing et al. (2022)
satellite observations
Huang et al. (2021)
ground observations
Kim et al. (2021)
BASE
ADJ

## Slide 8
Objective: Adjusting Gaseous and Particulate Matter Emissions
The current methods for adjusting particulate matter emissions, which can affect PM2.5 and PM10 concentrations, are limited.
(Kang et al., 2024; Kim et al., Under review)
Adjusting gaseous and particulate matter emissions based on ground observation data
China's rapidly changing emissions are regarded as a moving target
Ground Observation sites
Abundant ground observations

## Slide 9
Modeling System
For the anthropogenic emissions inventory, we used SIJAQ version 2 for the upwind and CAPSS 2021 for the downwind, with 2021 as the base year for both.
We applied a 27-km horizontal grid resolution for the upwind region and a 9-km resolution for the downwind region
FNL
Modeling Domain
Methods: Modeling System and Domain

## Slide 10
Methods: Adjusting Emissions Approach
Chart: Sensitivity
| 0.5 | 1
Concentration | 10 | 15
Concentration
Li et al. (2022)
1st Emission Adjustment
2nd Emission Adjustment: for remaining discrepancies
10

## Slide 11
Overview
BASE
(simulated using Emission Inventory)
Upwind (China)
Downwind (South Korea)
Adjust emissions based on
ground observations
ADJ
(simulated using Adjusted Emissions)
Methods: Sequential Adjustments of Upwind and Downwind Emissions
After adjusting upwind emissions based on ground observation concentrations, downwind emissions are subsequently corrected.
Kim et al. (2024)
TEA method

## Slide 12
Methods: Adjusted Emission Pollutants
Pollutants
Emission type | Emissions | Concentrations
Gaseous | CO | CO
 | SO2 | SO2, Sulfate
 | NO, NO2 | NO, NO2, Nitrate
Primary aerosol | Primary PM2.5 | Primary PM2.5
 | PMC | PM10
Given that gaseous concentrations affect the secondary formation of particulate matter, we corrected particulate emissions sequentially after adjusting gaseous emissions.

## Slide 13
Results: Emission Adjustment Results in China from 2015 to 2023
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
MB: -431.0 ppb
MB: -8.5 ppb
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
MB: -0.2 ppb
MB: -4.6 ppb
MB: 1.5 ppb
MB: 0.1 ppb
Upwind (China)
After the adjustment, the correlation coefficient and mean bias (MB) improved.
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 14
Results: Emission Adjustment Results in China from 2015 to 2023
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
MB: -11.1 ㎍/㎥
MB: -22.7 ㎍/㎥
MB: 5.1 ㎍/㎥
MB: 6.4 ㎍/㎥
Upwind (China)
Random error ▼
Systematic error O
Over-estimate
This method only considered each area's emission impacts on its own concentrations, so it did not account for inter-provincial interactions
Notes: Although the emission adjustments were applied twice consecutively, which accounted for some transport, the interactions between regions were not fully considered

## Slide 15
Results: Emission Adjustment Results in China from 2015 to 2023
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
MB: -11.1 ㎍/㎥
MB: -22.7 ㎍/㎥
MB: 5.1 ㎍/㎥
MB: 6.4 ㎍/㎥
Upwind (China)
Random error ▼
Systematic error O
Over-estimate
This method only considered each area's emission impacts on its own concentrations, so it did not account for inter-provincial interactions
Notes: Although the emission adjustments were applied twice consecutively, which accounted for some transport, the interactions between regions were not fully considered

## Slide 16
Results: Emission Adjustment Results in BR from 2015 to 2023
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
Nitrate
Sulfate
― EI-based ― Adjusted_Up
― EI-based ― Adjusted_Up
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 17
Results: Emission Adjustment Results in BR from 2015 to 2023
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
Nitrate
Sulfate
― EI-based ― Adjusted_Up
― EI-based ― Adjusted_Up
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 18
Results: Emission Adjustment Results in South Korea from 2015 to 2023
― EI-based ― Adjusted_Up ― Adjusted_Down
After the adjustment, the correlation coefficient and mean bias (MB) improved.
Downwind (South Korea)
EI-based
Adjusted_Up
Adjusted_Down
― EI-based ― Adjusted_Up ― Adjusted_Down
― EI-based ― Adjusted_Up ― Adjusted_Down
EI-based
Adjusted_Up
Adjusted_Down
EI-based
Adjusted_Up
Adjusted_Down
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 19
Results: Emission Adjustment Results in South Korea from 2015 to 2023
MB: -11.1 ㎍/㎥
MB: 5.1 ㎍/㎥
Random error ▼
Systematic error O
Over-estimate
Downwind (South Korea)
― EI-based ― Adjusted_Up ― Adjusted_Down
EI-based
Adjusted_Up
Adjusted_Down
― EI-based ― Adjusted_Up ― Adjusted_Down
EI-based
Adjusted_Up
Adjusted_Down
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 20
Results: Emission Adjustment Results in South Korea from 2015 to 2023
MB: -11.1 ㎍/㎥
MB: 5.1 ㎍/㎥
Random error ▼
Systematic error O
Over-estimate
Downwind (South Korea)
― EI-based ― Adjusted_Up ― Adjusted_Down
EI-based
Adjusted_Up
Adjusted_Down
― EI-based ― Adjusted_Up ― Adjusted_Down
EI-based
Adjusted_Up
Adjusted_Down
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 21
Results: Comparison of Emission Changes Between Bottom-Up and Top-Down Approaches
Chart: Upwind (China)
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
EI-based | 1 | 1.003 | 0.99977 | 0.99977 | 0.99994 | 1.0033 | 0.9999 | 0.99971 | 0.99977
CO | 6.2182 | 6.117 | 5.8085 | 5.2222 | 4.5425 | 4.072 | 3.9209 | 3.6435 | 3.6571
NOx | 3.0349 | 3.02 | 3.0799 | 2.893 | 2.7649 | 2.3901 | 2.2748 | 2.0959 | 2.1364
SO2 | 1.877 | 1.7622 | 1.4391 | 1.2225 | 0.92919 | 0.8417 | 0.83798 | 0.8477 | 0.80837
Primary PM2.5 | 6.6495 | 5.9682 | 5.6217 | 5.374 | 4.247 | 2.8475 | 2.8262 | 2.5045 | 2.7379
Chart: Downwind (South Korea)
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
EI-based | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
CO | 15.3636 | 15.0641 | 15.5513 | 15.9615 | 17 | 16.141 | 16.6282 | 14.6026 | 14.7564
NOx | 2.163 | 2.2065 | 2.087 | 1.9565 | 1.9891 | 1.7174 | 1.7609 | 1.6739 | 1.5543
SO2 | 2.2632 | 2.1053 | 2.1579 | 2.3684 | 2.3158 | 2.1053 | 2.3684 | 2.1053 | 2
Primary PM2.5 | 8.3333 | 8 | 6.3333 | 7 | 6.3333 | 5 | 4.6667 | 4.3333 | 5
Chart: Upwind (China)
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
CO | 1 | 0.98781 | 0.93487 | 0.84086 | 0.73141 | 0.65753 | 0.63124 | 0.58689 | 0.58911
NOx | 1 | 0.99795 | 1.0153 | 0.95402 | 0.91196 | 0.79021 | 0.75006 | 0.6913 | 0.70477
SO2 | 1 | 0.9388 | 0.76669 | 0.65131 | 0.49503 | 0.44842 | 0.44644 | 0.45162 | 0.43066
Primary PM2.5 | 1 | 0.89755 | 0.84544 | 0.80818 | 0.63869 | 0.42823 | 0.42503 | 0.37665 | 0.41174
Chart: Downwind (South Korea)
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
CO | 1 | 0.99324 | 1.0254 | 1.0524 | 1.1209 | 1.0642 | 1.0964 | 0.96281 | 0.97295
NOx | 1 | 1.0201 | 0.96482 | 0.90452 | 0.9196 | 0.79397 | 0.81407 | 0.77387 | 0.71859
SO2 | 1 | 0.93023 | 0.95349 | 1.0465 | 1.0233 | 0.93023 | 1.0465 | 0.93023 | 0.88372
Primary PM2.5 | 1 | 0.96 | 0.76 | 0.84 | 0.76 | 0.6 | 0.56 | 0.52 | 0.6
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 22
Additional
Re-adjust primary PM2.5 emissions for each of the five regions in China to reduce the overestimation of PM2.5.
The ratio of observed to simulated PM2.5 concentrations was applied to primary PM2.5 emissions, followed by re-simulation.
Additional simulation
COT
BTH
NEC
NRB
BTH
Methods: Correction of Systematic Bias
Notes: 5개 지역으로 나누어 Systematic 한 바이어스를 다ㅣㅅ 배출량에 곱해서 재산정해싿.

## Slide 23
Comparison of Observed and Simulated PM2.5 Concentrations in China for 2023
Over-estimate
MB: 4.7 ㎍/㎥
MB: -5.2 ㎍/㎥
EI-based
Adjusted_Up
― EI-based ― Adjusted_Up
Upwind (China)
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 24
Comparison of Observed and Simulated PM2.5 Concentrations in China for 2023
Over-estimate
MB: 4.7 ㎍/㎥
MB: -5.2 ㎍/㎥
MB: 0.5 ㎍/㎥
EI-based
Adjusted_Up
Adjusted_Up2
― EI-based ― Adjusted_Up ― Adjusted_Up2
The overestimation of PM2.5 has been reduced
Upwind (China)
Notes: 그 결과 배출량은 이런식으로 산정이 되었고 농도는 이렇게 되었다.

## Slide 25
Comparison of Observed and Simulated PM2.5 Concentrations in China for 2023
EI-based
Adjusted_Up
Adjusted_Up2
The simulated PM2.5 concentrations using adjusted emissions were more similar to observed values in high PM2.5 regions compared to the EI-based approach.
The spatial distribution in the simulation, referred to as Adjusted_Up2, was more consistent with the observations
Over-estimations
Under-estimations
Upwind (China)

## Slide 26
Conclusions
While the current focus has been on aligning PM2.5 mass concentrations using primary PM2.5 emissions, the next step is to apply an approach aimed at adjusting the PM2.5 component concentrations.
We developed emission adjustment methods based on ground observations in both upwind and downwind areas of Northeast Asia.
After adjusting the emissions, the simulated gaseous and particulate matter concentrations more closely matched the observations.
However, the simulated PM2.5 concentrations were initially overestimated compared to the observed values.
Next Steps