## Slide 1
Enhancing Meteorological and Air Quality Prediction Accuracy Through High-Resolution Data Assimilation Using Deep Learning
Hossein Alizadeh , Ali Azimi , Seyed Hamid Delbari , Vahid Hosseini
School of Sustainable Energy Engineering, Simon Fraser University, British Columbia, Canada

## Slide 2: Outline
06
07
01
02
03
04
05
CMAQ Results
Conclusion
Study Area
Methodology-Data Assimilation in WRF
Methodology-AI Integration
WRF Results
Motivation and Background
08
AI Results

## Slide 3: Motivations
Reduce bias errors with specific attention to extreme weather conditions in Edmonton, Alberta
Analyze the impact on CMAQ outputs
Nudging the model output for long-duration modelling
Improve the surface-level meteorological parameters where small-scale weather phenomena are important
Incorporate a novel AI downscaling method to reconstruct the grid analysis
Improve WRF Performance
Enhance Long-term Prediction Accuracy
Refine Local Forecast
Enhance AQ Prediction
Leverage Deep Leaning Downscaling

## Slide 4: Study Area
References:
www.alberta.ca
Edmonton is the capital of Alberta and is recognized as the fifth-largest city in Canada. Its population is approximately 1 million.
Edmonton's primary industrial activities include advanced technology, energy, and tourism. It is located in South Alberta, near Canada’s oil and gas reserves and industries.

## Slide 5: Local Air Quality Regulations
References:
https://www.casahome.org/attachments/CAAQS%20and%20NO2%202018-08-09.pdf
Canadian Ambient Air Quality Standards (CAAQS)
In terms of federal limits, all Alberta’s air zones have exceeded the 2020 NO2 CAAQS. Most of them are categorized in red management level.
An updated standards for NO2 concentration will be in effect starting 2025, in which annual average NO2 threshold will be reduced from 17 ppb to 12 ppb.
CAAQS Status

## Slide 6: WRF Data Assimilation
Variables to Nudge
Nudging Coeff.
Apply Weightings
Compute Nudging Tendency
Update Model
Advance to next time step
WRF Output
(WRF Data Assimilation)
GFS
1 degree
NCEP NAM
12 km
High-Res. Field
1.3 km
Field Variables Processing
MET Files
(AI Model)
Encoder
Decoder
NCEP: National Centers For Environmental Prediction
NAM: North American Mesoscale Forecast System
GFS: Global Forecast System
Notes: The Output of AI model includes field variables such as pressure, temperature, wind components, and moisture variables, which are structured in a way that WRF can efficiently read and process.
There is a Quality control procedure that involve gross error checks to identify and eliminate observations that fall outside the plausible range of meteorological variables, buddy checks to compare each observation with neighboring observations to detect inconsistencies or anomalies, and cross-validation against a background field to identify and discard data that significantly deviate from expected values.
The timing of applying nudges to the model defines the interval between the updates of nudging tendency terms and the assimilation of new observations.
The fundamental concept in observation nudging is the calculation of innovations, which represent the differences between observed values and the model's corresponding variables at the observation locations.
The weightings in nudging process ensures observations influence the model state appropriately in space and time. The overall nudging incorporates temporal, vertical, and horizontal weighting functions. Vertical weighting functions vary based on the observation type and the structure of the planetary boundary layer, and horizontal weighting involves calculating a radius of influence and applying a distance-based weighting function to modulate the influence.
Once the nudging tendencies are computed using innovations and weighting functions, these tendencies are added to the model's prognostic equations as additional forcing terms. This process gradually adjusts the model variables toward the observed values without abrupt changes that could destabilize the model.

## Slide 7: Methodology-Data Assimilation in WRF
  Stage 1:
  Train the model using data from 108 km to 12 km resolution
  Stage 2:
  Use the same trained model to downscale from 12 km to 1.33 km resolution
Deep Learning
Framework
Trained Model
108km
12km
12km
1.3km
Notes: As mentioned, in order to improve the accuracy of the WRF model, we need high-resolution climate data as input for its data assimilation process.
Such data is often unavailable, especially at finer scales like 1 km. So we tried to come up with a deep learning framework that could generate this high-resolution data by downscaling coarser inputs.
The model operates in two stages:
Stage 1: We train the model using data from 108 km to 12 km resolution.
Stage 2: The same model is then used to downscale from 12 km to 1.33 km.

## Slide 8: Methodology-AI Flow Chart
Encoder
Bottleneck
Decoder
Input
Output
Challenge:
  The relationship between coarse (108 km) and medium (12 km) resolutions is different from the relationship between 12 km and 1.33 km
Model Architecture:
  Residual Encoder-Decoder with Attention Mechanism
  Residual Learning helps by allowing the model to focus on refining the errors from an initial interpolation, rather than predicting the full high-resolution output.
  Model predicts residuals (corrections to bilinear interpolation), refining finer details to improve output resolution
Notes: The challenge is that the relationship between coarse (108 km) and medium (12 km) resolutions is different from the relationship between 12 km and 1.33 km. This makes it difficult for the model to learn general features that apply well across both scales.
To address this, we developed a Residual Encoder-Decoder with Attention Mechanism.
Residual Learning helps us by allowing the model to focus on refining the errors from an initial interpolation, rather than predicting the full high-resolution output. Which at this case, makes the learning process more efficient and accurate. Additionally, we used an Attention Mechanism which ensures the model focuses on the most important spatial features during downscaling, which results in capturing finer details that are crucial for improving WRF's performance.
So, we want to predict f^-1 which is the final high-resolution.
The bilinear interpolation is the initial estimate,
And finally the residual 𝑟 ( 𝑓 ^ − 1 ( 𝑋 ) ) is the correction the model learns to apply,

## Slide 9: Results – Temperature (K)
Mean Absolute Error | Root Mean Square Error | R2 Score
0.94 | 1.24 | 98.4%
Comparing the model's temperature prediction to the ground truth using statistical indicators
Results from Stage 1: Downscaling from 108 km to 12 km

## Slide 10: U - component of the velocity field
Mean Absolute Error | Root Mean Square Error | R2 Score
0.34 | 0.58 | 93.1%
Comparing the model’s U-component velocity prediction to the ground truth using statistical indicators
Results from Stage 1: Downscaling from 108 km to 12 km

## Slide 11: V - component of the velocity field
Mean Absolute Error | Root Mean Square Error | R^2 Score
0.44 | 0.65 | 91.8%
Results from Stage 1: Downscaling from 108 km to 12 km
Comparing the model’s V-component velocity prediction to the ground truth using statistical indicators

## Slide 12: Downscaling Outputs with the AI model
Temperature
U velocity component
V velocity component
Coarse to Fine Resolution:
108 km: Coarse patterns with minimal detail.
12 km: Intermediate resolution revealing more structure.
1.3 km: High-resolution output capturing fine-scale spatial variability critical for localized weather predictions.
12 km
1.3 km
108 km

## Slide 13: Methodology-Domain Specifications
D1
D2
D3
Domain | Lat_ref | Long_ref | Resolution (km)
Domain 1 | 49.48 | -120.73 | 9
Domain 2 | 52.37 | -115.51 | 3
Domain 3 | 53.21 | -114.06 | 1

## Slide 14: Methodology-WRF Model Flow Chart
Atmospheric and Land-soil variables
Land-use and topography data
Data preparation and conversion
Interpolation of data to the WRF domain
Initial/Boundary condition identification
WRF model
Simulation Episode:
12 Jul. – 24 Jul. 2019

## Slide 15: Methodology-CMAQ Model Flow Chart
Meteorology Chemistry Interface processor
Clear-Sky photolysis rates
Chemical Mechanism
Carbon Bond 6 version r3 with aero7 treatment of SOA
Anthropogenic emission
3-D Advection Scheme
WRF_CONS [7]
Vertical Diffusion
ACM2 Model [8]
Dry Deposition
M3DRY Model [9]
Emissions Chemistry Interface processor
Biogenic emission
Initial/Boundary Conditions
WRF Model
BEIS Model
SMOKE Model
CMAQ model
Canada National Emission Inventory (2015)
BELD4 Canada Land Use

## Slide 16: Methodology-Validation Process
Hourly observation data from 12 air quality monitoring stations operated by Alberta Capital Airshed was collected.
Ground-level hourly averaged model results were compared to the observation results.

## Slide 17: WRF Results – Temperature
Model | ME | RMSE | R
Base Case | 1.51 | 1.87 | 0.92
DA with AI | 1.37 | 1.75 | 0.92
DA with NCEP | 1.43 | 1.79 | 0.92
Model | ME | RMSE | R
Base Case | 1.51 | 1.87 | 0.92
DA with AI | 1.37 | 1.75 | 0.92
DA with NCEP | 1.43 | 1.79 | 0.92
Model | ME | RMSE | R
Base Case | 1.78 | 2.12 | 0.93
DA with AI | 1.73 | 2.05 | 0.93
DA with NCEP | 1.81 | 2.11 | 0.93
Model | ME | RMSE | R
Base Case | 1.78 | 2.12 | 0.93
DA with AI | 1.73 | 2.05 | 0.93
DA with NCEP | 1.81 | 2.11 | 0.93
St. Albert Station
Edmonton East Station

## Slide 18: WRF Results – Wind Speed
Model | ME | RMSE | R
Base Case | 1.21 | 1.65 | 0.58
DA with AI | 1.05 | 1.36 | 0.57
DA with NCEP | 1.13 | 1.45 | 0.61
Model | ME | RMSE | R
Base Case | 1.21 | 1.65 | 0.58
DA with AI | 1.05 | 1.36 | 0.57
DA with NCEP | 1.13 | 1.45 | 0.61
Model | ME | RMSE | R
Base Case | 1.47 | 1.85 | 0.68
DA with AI | 1.27 | 1.56 | 0.63
DA with NCEP | 1.41 | 1.81 | 0.69
Model | ME | RMSE | R
Base Case | 1.47 | 1.85 | 0.68
DA with AI | 1.27 | 1.56 | 0.63
DA with NCEP | 1.41 | 1.81 | 0.69
St. Albert Station
Edmonton East Station

## Slide 19: WRF Results
Line Contour of Temperature (k)
Contour of Wind Speed (m/s)
Data Assimilation Using AI Results
Data Assimilation Using NCEP NAM
Base Case

## Slide 20: CMAQ Results – NO2
Model | MAPE | RMSE | IOA
Base Case | 0.68 | 0.009 | 0.45
With DA using AI | 0.71 | 0.009 | 0.49
Model | MAPE | RMSE | IOA
Base Case | 0.68 | 0.009 | 0.45
With DA using AI | 0.71 | 0.009 | 0.49
Model | MAPE | RMSE | IOA
Base Case | 0.81 | 0.01 | 0.52
With DA using AI | 0.75 | 0.008 | 0.58
Model | MAPE | RMSE | IOA
Base Case | 0.81 | 0.01 | 0.52
With DA using AI | 0.75 | 0.008 | 0.58
Edmonton East Station
St. Albert Station

## Slide 21: CMAQ Results – PM 2.5
Model | MAPE | RMSE | IOA
Base Case | 0.45 | 7.7 | 0.33
With DA using AI | 0.43 | 6.2 | 0.55
Model | MAPE | RMSE | IOA
Base Case | 0.45 | 7.7 | 0.33
With DA using AI | 0.43 | 6.2 | 0.55
Model | MAPE | RMSE | IOA
Base Case | 0.47 | 7.7 | 0.40
With DA using AI | 0.42 | 5.8 | 0.62
Model | MAPE | RMSE | IOA
Base Case | 0.47 | 7.7 | 0.40
With DA using AI | 0.42 | 5.8 | 0.62
Edmonton East Station
St. Albert Station

## Slide 22: CMAQ Results – O3
Model | MAPE | RMSE | IOA
Base Case | 0.18 | 0.009 | 0.71
With DA using AI | 0.16 | 0.008 | 0.75
Model | MAPE | RMSE | IOA
Base Case | 0.18 | 0.009 | 0.71
With DA using AI | 0.16 | 0.008 | 0.75
Model | MAPE | RMSE | IOA
Base Case | 0.15 | 0.0076 | 0.82
With DA using AI | 0.14 | 0.0071 | 0.83
Model | MAPE | RMSE | IOA
Base Case | 0.15 | 0.0076 | 0.82
With DA using AI | 0.14 | 0.0071 | 0.83
Edmonton East Station
St. Albert Station

## Slide 23: Conclusion
01
03
02
04
Using the data assimilation method increased the accuracy of the model and reduced the errors of the WRF model. It utilizes the benefits of both mesoscale and local models by including the effects of a global model in a local model.
An encoder-decoder AI-based algorithm is used to nudge the WRF’s temperature and velocity fields into high-resolution, urban community-scale outputs.
Comparing the results of data assimilation using a high-resolution field for data assimilation increases the accuracy by reducing the mean error by 9%, while using a low-resolution field (NCEP) increases the accuracy by 4%.
The results of CMAQ indicated that while using more accurate meteorology data can enhance the accuracy of the model at specific times, other inputs, such as emission inventory, need to be dealt with separately.

## Slide 24: Acknowledgment
Environment and Climate Change Canada (ECCC), Climate Action Awareness Fund (CAAF)—Advancing Climate Change Science & Technology, provides the funding for the project “Urban Transportation Emissions and GHGs; Technologies and Behavioral Shifts.”
Research collaborators at the University of Alberta, Prof. Bob Koch and Prof. Mahdi Shahbakhti.
Project partners, such as the Government of Alberta, the City of Edmonton, Clean Air Strategic Alliance, and Alberta Airshed Council.
Research students at the CREATE lab, School of Sustainable Energy Engineering, Simon Fraser University, Metro Vancouver, Canada
Collaborative Research on Energy, Air Pollution, Transportation and Environment

## Slide 25: Thank You for Your Attention
Email
Haa59@sfu.ca

## Slide 26: Back up slides – CMAQ time series

## Slide 27: CMAQ Results – NO2
Model | MAPE | RMSE | IOA
Base Case | 0.68 | 0.009 | 0.45
With DA using AI | 0.71 | 0.009 | 0.49
Model | MAPE | RMSE | IOA
Base Case | 0.68 | 0.009 | 0.45
With DA using AI | 0.71 | 0.009 | 0.49
Model | MAPE | RMSE | IOA
Base Case | 0.81 | 0.01 | 0.52
With DA using AI | 0.75 | 0.008 | 0.58
Model | MAPE | RMSE | IOA
Base Case | 0.81 | 0.01 | 0.52
With DA using AI | 0.75 | 0.008 | 0.58
Edmonton East Station
St. Albert Station

## Slide 28: CMAQ Results – PM 2.5
Model | MAPE | RMSE | IOA
Base Case | 0.45 | 7.7 | 0.33
With DA using AI | 0.43 | 6.2 | 0.55
Model | MAPE | RMSE | IOA
Base Case | 0.45 | 7.7 | 0.33
With DA using AI | 0.43 | 6.2 | 0.55
Model | MAPE | RMSE | IOA
Base Case | 0.47 | 7.7 | 0.40
With DA using AI | 0.42 | 5.8 | 0.62
Model | MAPE | RMSE | IOA
Base Case | 0.47 | 7.7 | 0.40
With DA using AI | 0.42 | 5.8 | 0.62
Edmonton East Station
St. Albert Station

## Slide 29: CMAQ Results – O3
Model | MAPE | RMSE | IOA
Base Case | 0.18 | 0.009 | 0.71
With DA using AI | 0.16 | 0.008 | 0.75
Model | MAPE | RMSE | IOA
Base Case | 0.18 | 0.009 | 0.71
With DA using AI | 0.16 | 0.008 | 0.75
Model | MAPE | RMSE | IOA
Base Case | 0.15 | 0.0076 | 0.82
With DA using AI | 0.14 | 0.0071 | 0.83
Model | MAPE | RMSE | IOA
Base Case | 0.15 | 0.0076 | 0.82
With DA using AI | 0.14 | 0.0071 | 0.83
Edmonton East Station
St. Albert Station