## Slide 1: Evaluating The Relationship of Modeled Meteorology and Ozone Bias using Random Forest Regression
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Oak Ridge Associated Universities National Student Services Contract
1
2
Disclaimer: The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA.

## Slide 2: Evaluation of EQUATES (2002-2019) CMAQ outputs has revealed an increasingly negative trend in modeled ozone bias in the eastern US on highest ozone days.
General low bias of model outputs at beginning of time series (2002-2007)
Low bias reemerges with increasingly negative trend in latter portion of EQUATES (2014-2019)
All sites East of 90° (~Mississippi river)
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Figure: C. Hogrefe (2023)

## Slide 3: WRF meteorology data available in the EQUATES domain allows for exploration of the relationship between WRF meteorology inputs and CMAQ modeled MDA8 O3.
This enables the investigations of:
  A.) Is bias in WRF modeled meteorology a potential driver of ozone bias?
  B.) Can trends in ozone bias be associated with trends in bias in meteorology?
  C.) Does the negative bias in ozone tend to occur during certain observed meteorological conditions?
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Feature | Unit | Time | Value Range | Bias (Modeled-Observed) Range
Maximum Daily Temperature | K | 8:00-20:00 | 240, 315 | -25, 25
Average Mid-day Water Vapor Mixing Ratio | g/kg | 10:00-16:00 | 0, 30 | -20, 20
Morning Wind Speed | m/s | 7:00-10:00 | 1.5, 25 | -10, 10
Afternoon Wind Speed | m/s | 13:00-16:00 | 1.5, 25 | -10, 10
Daily Precipitation (PRISM Obs. Data*) | mm/day | Full Day | 0, Obs. Max | -50, 50
Quality Control and compilation of Daily WRF Meteorology Features
Features Derived from Wells et al. (2021)
*Non-WRF; not included in Wells et al.

## Slide 4: Paired meteorology-MDA8 O3 data is grouped into NOAA climate regions.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Max. Daily Temperature (K)
Daytime Water Vapor Mixing Ratio (g/kg)
Trends in modeled meteorology closely match those in observed meteorology throughout ozone season (left) and on top 10 modeled ozone days (right).
This is expected due to use of data assimilation in the WRF modeling via nudging.
Daytime Water Vapor Mixing Ratio (g/kg)
Max. Daily Temperature (K)

## Slide 5: Paired meteorology-MDA8 O3 data is grouped into NOAA climate regions.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Max. Daily Temperature (K)
Daytime Water Vapor Mixing Ratio (g/kg)
WRF model is slightly cooler and more humid than observations in some regions/years.
On the highest observed ozone days there is more bias in modeled mixing ratio than temperature. Mixing Ratio is not nudged as strongly as temperature.
Daytime Water Vapor Mixing Ratio (g/kg)
Max. Daily Temperature (K)

## Slide 6: Random Forest (RF) Regression models are developed regionally to evaluate the predictive power of meteorology features in capturing ozone bias throughout peak ozone season (May-September).
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Feature Permutation evaluates relative importance of each feature independent of all other features.
Optimized model versions are trained on bias in met features as well as spatio-temporal features (land/water classification, Lat./Lon., Month, Year) included as surrogates for other drivers of model ozone bias.
Best predictors of ozone bias are year and month, indicating bias in modeled meteorology is not a primary driver for ozone bias.
Bias in temperature and mixing ratio have more predictive power than bias in windspeed and precipitation.
Feature Importance
Model Score decrease (MSE)
RF Features
Temperature Bias
Mixing Ratio Bias
Afternoon WS Bias
Morning WS Bias
Precipitation Bias
Non-WRF Bias Surrogates
Model Month/Year

## Slide 7
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Northeast Region
Ohio Valley Region
Southeast Region
Y = Partial Dependence = Average O3 Bias Prediction at X value

## Slide 8
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Northeast Region
Ohio Valley Region
Southeast Region
Y = Partial Dependence = Average O3 Bias Prediction at X value
Predictive power shown by any (non-zero) trends across Feature Value Range (X-axis). Features with higher predictive power have greater ozone bias distributions as X values increase.
Month
Month
Month
Temp. Bias
Temp. Bias
Temp. Bias
Q Bias
Q Bias
Q Bias

## Slide 9
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Northeast Region
Ohio Valley Region
Southeast Region
Y = Partial Dependence = Average O3 Prediction at X value
Consistent trend across regions in model years, decreasing ozone bias in later half of time series
High predictive power shown in Month across regions, with low-to-negative ozone bias being prominent in early ozone season months

## Slide 10
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Northeast Region
Ohio Valley Region
Southeast Region
Y = Partial Dependence = Average O3 Prediction at X value
Temperature and Mixing Ratio Bias each show a relationship with ozone bias at greater values for most regions, but unable to predict ozone bias at negative values.
Wind Speed, Precipitation have very little relationship with ozone bias.

## Slide 11: The trained feature importance inherited by RF models allows for investigation into feature relationships with ozone bias through time.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
2-way Partial Dependence Analysis:
- Avg. X in subset(Year): ~2006
- Avg. Y in subset (Month): ~8.0
- Avg. predicted O3 Bias: 3.61-5.59 ppb
Many decision trees (ML sub-models) in a Random Forest predict O3 bias by splitting data into random subsets (random feature value distributions)
Contour Interpretation:
  For a subset with a given average Feature X (Year) and average Feature Y (Month), the model makes an average O3 bias prediction.
Northeast Region

## Slide 12: The trained feature importance inherited by RF models allows for investigation into feature relationships with ozone bias through time.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
2-way Partial Dependence Analysis (Idealized Scenarios):
Temp. Bias
Temp. Bias
Temp. Bias
Temp. Bias
O3 Bias
Insignificant (~0) correlation
Temp. Bias perfectly correlated to Ozone Bias
i.e., horizontal contours indicate Temp. Bias is a ‘perfect’ predictor of Ozone Bias with no temporal change.
Converging Trend in Negative and Positive Bias.
i.e. stronger predictive power in later model years.
Temp. Bias
Temp. Bias
Temp. Bias
O3 Bias
O3 Bias
O3 Bias
Year = 2002
Year = 2011
Year = 2019
Year = 2002-2019

## Slide 13: Partial Dependence Analysis
In the Eastern US low ozone bias tends to occur in spring months, May – June.
The magnitude of this low bias increases at the end of the timeseries, consistent with the boxplots shown earlier.
The Southeast shows the largest ozone overestimation of the three regions, with high bias peaking in July/August of 2002-2005.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Ozone bias as a function of Month and Year
O3 Bias (ppb)
Northeast
Ohio Valley
Southeast
Month
Month
Month

## Slide 14: Partial Dependence Analysis
Northeast:
  Mixing Ratio/Temp. Bias associated with positive ozone bias at positive values (horizontal contours).
  Negative bias in both negative mixing ratios and temps. begins to be associated with some negative ozone bias in 2015-2019. No strong linear relationship (lack of horizontal contours).
Southeast:
  Little to no relationship between mixing ratio and temperature bias in all conditions (vertical contours).
Ohio Valley:
  Association between mixing ratio bias and ozone bias changes from year to year.
  Temp. bias remains a powerful predictor of positive ozone bias only, and only at positive values.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Ozone bias as a function of Temp./Q Bias and Year
O3 Bias (ppb)
Northeast
Ohio Valley
Northeast
Ohio Valley
Southeast
Southeast
Mixing Ratio Bias
Temperature Bias

## Slide 15
Evaluating how well the RF model captures explained variability (R2 score) in ozone bias across regions shows:
  The combination of WRF and non-WRF features captures up to 45-55% of the explained variability in modeled ozone bias (additionally serving as a baseline for future investigations)
  The relationship between WRF meteorology bias and ozone bias is stronger in the Northeast, Ohio Valley, South, Southwest, and West (relative to other regions).
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Non-WRF | WRF Only | ‘Integrated’
Year | Temp. Bias | All Features
Month | Q Bias | 
Latitude | Morning WS Bias | 
Longitude | Afternoon WS Bias | 
Grid Bias | Precip. Bias | 
Land Class. |  | 

## Slide 16: The RF model captures a low ozone bias concurrent with higher temperature and lower mixing ratios, consistent with ground truth data.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Obs. Mixing Ratio (g/kg)
Obs. Mixing Ratio (g/kg)
Obs. Max. Temperature (K)
Obs. Max. Temperature (K)
Year
Northeast Region
Ground truth
A separate RF model was fit using observed meteorology (rather than met bias).
CMAQ generally over-predicts ozone in very humid conditions and generally under-predicts ozone in hot and dry conditions.

## Slide 17: Summary and Future Development
Bias in meteorology was found to have a weak association with ozone bias and does not explain the increase in negative bias at the end of the time series.
Future work
Investigate other possible meteorological drivers of ozone bias such as solar radiation and cloud cover
Train RF model on high ozone days only
Incorporate emissions information
   While there is currently no direct emissions bias data, we can use source contribution to modeled ozone concentrations (based on CMAQ ISAM modeling) to explore if negative ozone bias is higher in conditions dominated by a certain source category (see table).
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
CMAQ v5.4 – Integrated Source Apportionment Method (ISAM) Species Categories:
Source Category | Source Category
US Mobile Onroad | US Mobile Nonroad
US Mobile airports, commercial marine vessels, rail | US Oil and Gas
US EGUs (Power Plants) | US Volatile Chemical Products
US Anthropogenic Fires | US Anthropogenic Other-All
Natural Sources | US Wildfires, all Canadian and Mexican fires
Canada and Mexico Anthropogenic Sources | Boundary Conditions

## Slide 18: References
EQUATES. (2024, March 24), https://www.epa.gov/cmaq/equates
Wells et al., 2021, “Improved estimation of trends in U.S. ozone concentrations adjusted for interannual variability in meteorological conditions”, Atmospheric Environment, https://doi.org/10.1016/j.atmosenv.2021.118234
The Integrated Source Apportionment Method (CMAQ-ISAM). (2024, Sept. 4), https://www.epa.gov/cmaq/integrated-source-apportionment-method-cmaq-isam
Scikit-learn: Machine Learning in Python, Pedregosa et al., JMLR 12, pp. 2825-2830, 2011.
  Random Forest Regressor [Computer Software], https://scikit-learn.org/stable/modules/generated/sklearn.ensemble.RandomForestRegressor.html
  Permutation feature importance [Computer Software], https://scikit-learn.org/stable/modules/permutation_importance.html
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch

## Slide 19: Additional Materials
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch

## Slide 20: A Random Forest (RF) Regression model is developed for each region to evaluate the predictive power of meteorology features in capturing ozone bias.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
A separate RF model was fit using observed meteorology (rather than met bias).
Generally, observed temperature and mixing ratio are best predictors for ozone bias.
Spatiotemporal features have a major influence (relative to other Met. features).
Feature Importance – Observed Met
Model Score decrease (MSE)

## Slide 21: While WRF Temperature and Mixing Ratio are associated with ozone bias, trends of these features are not as strong as that seen in ozone bias.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
O3 Bias (ppb)
Max. Temp. (K)
Mixing Ratio (g/kg)
Northeast Region

## Slide 22: While WRF Temperature and Mixing Ratio are associated with ozone bias, trends of these features are not as strong as that seen in ozone bias.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
O3 Bias (ppb)
Max. Temp. (K)
Mixing Ratio (g/kg)
Northeast Region
v
Lat.
Lon.
Year
Month
Obs. Temp.
Obs. Mix. Ratio
Elevation Bias
Obs. Wind Speed (morn.)
Obs. Wind Speed (aft.)
Land Class.
Obs. Precip.

## Slide 23: Overall, the bias and observed conditions in the most notable meteorology features reveal no matching trends to that seen in ozone bias.
Center for Environmental Measurement and Modeling, Atmospheric & Environmental Systems Modeling Division, Atmospheric Dynamics and Meteorology Branch
Northeast Region
Year
Mixing Ratio Bias (g/kg)
Temperature Bias (K)
Obs. Mixing Ratio (g/kg)
Obs. Max. Temperature (K)
Year
Ground truth density of average yearly values.
No trends shown, limitations on model prediction domain shown (95 % of data)

## Slide 24: Interpreting 1-way Partial Dependence Plots
Lat.
Lon.
Year
Month
Obs. Temp.
Obs. Mix. Ratio
- Avg. X in subset(Year): ~2005
- Avg. predicted O3 Bias: ~ 2 ppb
- X ticks show the decile ranges (every 10% of data volume) of the X feature