## Slide 1: Timely Updates of Anthropogenic Emissions with Satellite and Ground Observations: Comparing of multiple rapid emission refresh methods
1 Department of Atmospheric, Oceanic and Earth Sciences, George Mason University, Fairfax, VA 22030, USA
2Center for Spatial Information Science and Systems, George Mason University, Fairfax, VA 22030, USA
3Goddard Earth Sciences Technology and Research (GESTAR) II, Morgan State University, Baltimore, MD 21251, USA
4NASA Goddard Space Flight Center, Greenbelt, MD 20771, USA
5Department of Civil and Environmental Engineering, University of Tennessee, Knoxville, TN 37996, USA
6Department of Earth and Environmental Sciences University of Texas at Arlington, Arlington, TX 76019, USA
Siqi Ma1, Daniel Tong1,2, Fei Liu3,4, Jia Xing5, Bok H. Baek2, Chi-tsan Wang2, Yunyao Li6

## Slide 2
Background
Emissions of air pollutants are the main driver of many Earth system processes, such as air pollution and climate change.
Creating emission inventories typically lags by 3 years which may not reflect the current emission status.
Updating emissions to the specific forecast year using observations is an effective way to reduce the uncertainties of outdated emission inventories.
Objectives:
1) Updating anthropogenic emissions with multiple rapid emission refresh methods;
2) Assessing the effectiveness of each method.
NEI | Release Date
2008v2 | Feb 2012
2011v1 | Jun 2014
2014v1 | Sep 2016
2017v1 | Sep 2019
2020 | Mar 2023
2023 | Mar 2026
NOx

## Slide 3
Method
With AirNOW and TROPOMI NO2 products, NOx emissions are projected from 2019 to 2020 using an adjustment factor (AF), which is described as (Tong et al., 2016):
where ΔS and NS are the changing rate and the number of satellite data. ΔG and NG are the changing rate and the number of ground-based data, respectively. And FS (=1) and FG (=100) are two weighting factors for the satellite and ground data.
NOx emissions refresh:
Model configuration:
Six Scenarios:
Control: Using base year emission (NEI2019 platform)
N2020: Using current year emission (NEI2020) released by EPA
ADJ: state-level AF based on AirNOW and TROPOMI.
Budget-Aware (BA): state-level AF with specific city AF masked by surface emission contribution (>90%) from process analysis. Each city mask has a maximum of 150×150 km2
SatNOx: state-level AF with city-level AF based on TROPOMI estimated NOx emission (Liu et al., 2024).
VAE: state/city-level AF based on machine learning (Variational AutoEncorder, VAE) emissions (Xing, et al., 2022).
Model Setup:
Model: WRFv4.0 for meteorological simulations
CMAQv5.3.2 for air quality simulations
Date: July, 2020
Domain: Contiguous United States (CONUS) 12 km
Meteorological: ECMWF ERA5, 0.25° × 0.25°, 4/day
Initial Conditions: CMAQ profile IC
Boundary Conditions: GEOS-Chem monthly data

## Slide 4
State- and City-level Adjustment Factors
ADJ NOx AF state
BA NOx AF urban mask
SatNOx NOx AF city
VAE NOx AF state & city
States in the west present a medium decline, while eastern states see significant reductions.
States in the central US present smaller decreases/increases.
AFs in cities and states may show opposite trends.

## Slide 5
Anthropogenic NOx Emissions in July 2020
NOx differences % (N2020-control)
NOx differences % (BA-control)
NOx differences % (ADJ-control)
NOx differences % (VAE-control)
NOx differences % (SatNOx-control)
NOx monthly emission (control)
tons/month
383 Gg
416 Gg
445 Gg
425 Gg
411 Gg
396 Gg
Emissions from NEI2020 in parts of TX/NM have increased.
ADJ/BA/SatNOx present less NOx change in the central US.
VAE yields the closest emission to NEI2020 over CONUS
N2020 | ADJ | BA | SatNOx | VAE
-13.7% | -6.9% | -5.7% | -7.1% | -10.4%
Changes compared to NEI2019

## Slide 6
Effects of Emission Refresh on Ozone Prediction
O3 differences (N2020-control)
O3 differences (ADJ-control)
O3 differences (SatNOx-control)
O3 differences (VAE-control)
O3 differences (BA-control)
N2020 shows the most decrease.
ADJ/BA/SatNOx: large O3 decrease in NC/SC; VAE: AZ/CA
O3 is generally underpredicted in the western US.
O3 (control) 202007

## Slide 7
Do They Improve the Ozone Prediction?
East: overestimation; West: underestimation.
Emission update improves ozone prediction in the eastern US.
Mean Bias reduction in CONUS: 2% (VAE) – 13% (SatNOx)
Yellow-Red: Bias
Blue: Bias ↓

## Slide 8
Taylor Diagrams and Skill Scores
TSS =
Regional scale:
Smaller deviations, moderate correlations.
Northern east/west > Southeast/Southwest > Central US > South
SatNOx outperforms in 6 out of 10 regions; BA shows the highest mean TSS.
City scale:
Bigger variabilities than the regional scale
East/Central > South/Southwest
VAE scores highest in 4 cities while SatNOx has the best overall performance.
EPA Regional Offices
Cities

## Slide 9
NO2 differences (N2020-control)
NO2 differences (ADJ-control)
NO2 differences (SatNOx-control)
NO2 differences (VAE-control)
NO2 differences (BA-control)
NO2 (control) 202007
Effects of Emission Refresh on NO2 Prediction
High differences in cities.
Increased NO2 appears in some cities (i.e. Chicago, IL; Buffalo, NY).
Urban NO2 is usually underestimated, MB increase: 1% (VAE) – 10% (SatNOx).

## Slide 10
NO2 Vertical Column Density
CMAQ-BA
TROPOMI
Difference
1015 molecules cm-2
Atlanta
Difference
TROPOMI
CMAQ-BA
CONUS
Simulations can reproduce the high VCDs in cities and facilities.
Biased-high in downtowns, VCD rapidly declines from urban to rural areas.
1015 molecules cm-2
Cities (50 km2)
EPA Regional Offices
Control run performs the best due to high NOx emissions.
NMBs in cities are smaller than in EPA regions, except N2020.
Regional scale: SatNOx
City scale: Budget-Aware (BA)

## Slide 11
Combine with other adjustment methods
Positive: NMB decrease; Negative: NMB increase
NMB of O3 presents a reduction of 11% (-7% → -6%),
and NO2 NMB reduces with a percentage of 15% (-25% → -21%).
The decreasing of NOx emission amplifies the model underprediction in the western US. A forward modeling method using NO2 VCD is applied for emission adjustment in Phoenix:
NMB change

## Slide 12
Conclusions
The updated emissions effectively reflect the NOx decrease trend in 2019–2020. VAE shows the nearest emission change (-10.4%) compared to NEI2020 (-13.7%).
The refresh methods reduce mean biases of modeled ozone by 2%–13% compared to the outdated emission inventory.
The Budget-Aware method outperforms at the regional scale and SatNOx performs better at the city scale.