## Slide 1: Improving numerical air quality forecasts in the western United States with an emphasis on wildfire smoke
Taylor Wilmot, Heather Holmes,
Derek Mallia, Kerry Kelly,
Ross Whitaker

## Slide 2: Outline
CREATE-AQI overview
Forecast model framework
Preliminary forecast evaluation
Future development
2

## Slide 3: CREATE – AQI
An NSF CIVIC project to observe and predict Utah air quality
Objective: protect Utah children from outdoor air quality hazards
  Combine air quality sensors and automated forecasts to inform decision makers
Wintertime inversions, windblown dust, and wildfire smoke are all present in Utah
CREATE-AQI Forecast model Preliminary evaluation Future development
3

## Slide 4: CREATE – AQI observations
Effectively a nowcasting tool
Installing sensors at high schools throughout the state
Employs ML to spatially interpolate
Long term: will be leveraged to improve forecasting outputs
4
CREATE-AQI Forecast model Preliminary evaluation Future development

## Slide 5
5
Whole atmosphere community climate model
Chem. initial/boundary conditions
Freitas et al. plume rise
Plume top heights
Vertical distribution of smoke
SMOKE modeling system
Hourly, 3-D, wildfire emissions grids
WRF simulation
12km met. simulation
CMAQ – forecast
National emissions inventory
Non-fire emissions
MCIP, ICON, BCON
Fire emissions prediction
Criteria pollutants
Heat fluxes, fire area
Forecast framework – air quality
CREATE-AQI Forecast model Preliminary evaluation Future development

## Slide 6
Forecast framework – wildfire emissions
Fire activity forecast model
Satellite detections
Criteria pollutants, fire area, heat flux based on EFs
Fuel moisture
Model computes dead and live fuel moisture to initialize fuel consumption model
Vegetation data
Provides gridded fuel characteristic data from LANDFIRE
Meteorological forecasts
WRF provides medium-resolution weather data
MODIS and VIIRS for magnitude, normalized GOES used for scaling
Rate of spread
Rothermel et al. (1972) model used to scale heat fluxes and fire area up or down
ROS
t
Fire area
forecast
spin-up
Fire emissions prediction
If its hotter, windier, and drier tomorrow, the model will scale up the fire area, heat flux and smoke emissions
GOES detection
VIIRS/MODIS detection
Fire forecast
Fire spin-up period
6
CREATE-AQI Forecast model Preliminary evaluation Future development

## Slide 7
Forecast framework – wildfire emissions
Satellite detections
Fuel moisture
Model computes dead and live fuel moisture to initialize fuel consumption model
Vegetation data
Provides gridded fuel characteristic data from LANDFIRE
Meteorological forecasts
WRF provides medium-resolution weather data
MODIS and VIIRS for magnitude, normalized GOES used for scaling
Rate of spread
Rothermel et al. (1972) model used to scale heat fluxes and fire area up or down
ROS
t
If it rains and is cooler tomorrow, the model will scale down the fire area, heat flux and smoke emissions
6
Fire area
forecast
GOES detection
VIIRS/MODIS detection
Fire forecast
spin-up
Fire spin-up period
Fire activity forecast model
Criteria pollutants, fire area, heat flux based on EFs
Fire emissions prediction
CREATE-AQI Forecast model Preliminary evaluation Future development

## Slide 8: Forecast framework – wildfire plume rise
7
Stand alone version of Freitas et al. plume rise scheme
Ingests forecasted heat flux, fire area, and meteorological fields
Entrainment – mass conservation approach to predict vertical distribution
FluxVertical, In
FluxVertical, Out
Entrainment
Detrainment
CREATE-AQI Forecast model Preliminary evaluation Future development

## Slide 9: Forecast framework – outputs
8
CREATE-AQI Forecast model Preliminary evaluation Future development

## Slide 10
Performed well for largest smoke event in Salt Lake City this summer
Issues with smoke emissions from cloud blocked fires
Timing and shape of smoke plumes appear better forecasted than magnitude of smoke
Forecasted PM2.5 values are biased high
9
Preliminary evaluation – air quality
Forecast
Observations
CREATE-AQI Forecast model Preliminary evaluation Future development

## Slide 11
10
Future development
WRF-CMAQ:
  4km nested domain
  Two-way coupling
Wildfire emissions:
  Number of possible development pathways (FOFEM, ML ingesting coupled models, etc.)
Wind blown dust:
  Inclusion of exposed lakebed in playa land use category (important for Great Salt Lake)
Wintertime inversions:
  Likely a statistical model that is initiated based on met conditions
Bias reduction scheme based on accompanying sensor observations
CREATE-AQI Forecast model Preliminary evaluation Future development
Questions: Kai.Wilmot@utah.edu