## Slide 1: Estimating Air Quality Exposure in 1940 and 2010 For Future Application to Health Analyses
Xiaorong Shan Advisor: Lucas Henneman
23rd CMAS Conference October 22 2024

## Slide 2
2
Emissions processes
Physical atmospheric processes
Chemical atmospheric processes
SOx
NOx
PM
NOx
CO
VOCs
NOx
EC
PM
VOCs
WIND
Deposition
NO
hv
RO2 /HO2
RO/OH
NO2
O2
O3
Ozone (O3)
HNO3
OH:
Daytime
Nighttime:
O3, H2O
NaCl
NaNO3
NH3
NH4NO3
SO2
H2SO4
OH:
Daytime
H2O2
OC
Particulates (PM2.5)
Three broad processes dictate air pollution exposure
Henneman CEIE 649

## Slide 3
Motivation: estimate and evaluate source-specific exposure in 1940
Why 1940?
Early-life air pollution exposure may increase the risk of cognitive decline and neurodegenerative diseases in late life.
Why source-specific?
Air pollution from different sources may pose varying risks to health.
Notes: Exposure assessment
  Approach: Quantify population exposure to specific air pollution sources in the U.S. in 1940 using available data and methods that appropriately account for emissions processes, physical processes, and chemical processes
  Evaluation: Apply comparable exposure estimates in a period with extensive observations (2010)

## Slide 4
Emissions
  Lack of accurate records in 1940
Exposure
  Reduce complexity models
Evaluation
  2010 standard monitor measurement
Research plan designed
Notes: I think it’s important to address that:
1) We want exposure estimates (including source-specific exposure)
2) There are times and places when it is difficult to estimate exposure (e.g., before air pollution observations throughout the US)
3) We need new ways to model exposure from these sources and evaluate the models

## Slide 5
Air pollution sources considered
Pollution source | Major Health-Related pollutants | % Total Emissions in 1940
Power Plants | SO2, NOx, PM and CO | 60% of SO2 emissions
Automobiles | NOx, CO and PM2.5 | 40% of NOx emissions
Wells of Oil & Gas | Methane, VOCs, NOx, PM2.5 | 15% of total PM2.5 emissions
Residential & Commercial Coal Combustion | SO2, CO2, PM2.5, CO | 25% of total PM2.5 emissions
National Air Pollutant Emission Estimates, 1940-1990 (US EPA)
Notes: Larger text
I don't think the Impact column is necessary, since each of these has many impacts
What if instead of Impacts you report the fraction of total 1940 emissions from each source in the US, per CMIP6? So, power plants were probably something like 60% of SO2 emissions; automobiles contributed something like XX% of NOx, etc.
Austin: for this research I am going to present the power plants, but the at the end I am going to show the exposure maps for different sources

## Slide 6
Fossil fuel power plants were a major air pollution sources in 1940
233 fossil fuel power plants were in operation in 1940 (EIA)
48 burned coal, 129 burned petroleum, and 56 burned natural gas
Contributed to 60% of SO2, 30% of NOx, 20% of PM, and 10% of CO emissions
No regulations in 1940 required emissions controls
EIA (Energy Information Administration)
Notes: Be clear for automobiles or vehicles
Make this 1940-centric. Some suggestions:
Title: Fossil fuel power plants were major air pollution sources in 1940
XX power plants were in operation in 1940 (EIA)
Of these, YY burned coal and ZZ burned natural gas
No regulations in 1940 required emissions controls
60% electricity?

## Slide 7
1940 power plant-level emissions factors derived using data in 2010
E1940 = A1940 x EF2010 x (1-ER1940/100)
Emission factors (EF2010)
Power plant emissions in 2010
Power plant facility info in 1940
EPA eGRID
EIA
ER1940 = 0
A1940
Power plant emissions in 1940
EPA eGRID (Environmental Protection Agency Emissions & Generation Resource Integrated Database)
EIA (Energy Information Administration)
Notes: Recommend larger text
Recommend building this slide piece by piece—then whole flow chart is overwhelming
LH: Note somehow that today's data is reliable because it is measured at each stack and reported to EPA

## Slide 8
Physical atmospheric processes: two approaches
Inverse Distance Weighted (IDW)
Assumption: equal dispersion of pollutant in all directions
=
Benefit: Simple and easy to apply
Drawback: dispersion does not reflect real-world conditions, especially in varying terrains
Unitless exposure
HYSPLIT Average Dispersion (HyADS)
Assumption: dispersion governed by atmospheric conditions and terrain influences
=
Benefit: accounting of atmospheric dispersion
Drawback: meteorological data represents 1940 climatic conditions
Physical unit [ug/m3]
Henneman et al. 2019 (Atmospheric Environment)
Notes: Recommend larger text
Recommend building this slide piece by piece—then whole flow chart is overwhelming
LH:
Recommend a slide introducing the 2 exposure methods to approximate the physical transport process (I added this above):
IDW assumes equivalent transport in all directions, and is often applied to assess point-source exposure
Trajectory models use wind fields to track pollution transport, but reanalysis wind fields available in 1940 are only representative
So, we apply both and compare

## Slide 9
Chemical Processes
From emissions parameterizations, we do know which chemicals are emitted
But applying a Chemical Transport Model like CMAQ would require lots of computation, and we don't have the observations to compare it against
We use statistical parameterizations for HyADS derived from Henneman et al. 2019 (Atmospheric Environment)
Notes: Power plants can highlight the project
Similar distribution exposure HyADS & IDW

## Slide 10
HyADS model setup for 1950
Account for 1951 to 1960 meteorology data (10 years)
Incorporate 1940 power plant estimations as input
Divide the entire U.S. mainland into different grid cells
Run the model to simulate dispersion and count air parcels in each grid cell to determine exposure
Notes: You might need an additional slide that describes your hyads approach - it's very cool that you ran the model accounting for 10 years' worth of meteorology since 1940 is just an estimate. Make sure that comes through!

## Slide 11
1940 power plant (PP) IDW and HyADS exposure comparison
90% of SO2 exposure originates from coal power plants
Coal is the dominant source of exposure relative to the other fuels
Power plant SO2 exposure is concentrated in the Midwest and Southeast regions
1940 PP IDW [unitless]
1940 PP HyADS [ug/m3]
Notes: Power plants can highlight the project
Similar distribution exposure HyADS & IDW
LH:
There are definite differences between HyADS & IDW - you can see much more "real"-looking dispersion patterns from HyADS

## Slide 12
1940 PP IDW coal
2010 PP IDW coal
1940 and 2010 power plant IDW exposure comparison
Normalize separately
Concentration magnitude:
  1940: 0.087 to 3.07, median 0.33
  2010: 1.88 to 17.88, median 7.25
Compared to 1940, 2010 shows higher exposure in the South than in the Midwest
Notes: Differences between maps
Having the location of the facility
Difference in magnitude: emissions source or the amount of emissions
Movitation: exposure, what driven the change of exposure in space and magnitude
Another slide for hydas 1940 & 2010

## Slide 13
Power plant IDW exposure evaluation with EPA monitor measurement in 2010
328 EPA monitors in total, different number of monitors for pollutant types
County-level exposure V.S. stationary measurement may cause different results
Notes: If possible, compare both hyads & idw by their performance with monitors
What about sulfate? That would be the most importtant one. Actually, you could safely present just sulfate and total PM2.5
First of all, we found a supervising negative R result for NOx, the county level exposure v.s. stationary measurement may cause different results. Pink is anything less than 0, blue is 0-0.5, and green is higher than 0.5
Do hyads and more than just correlation legend (IDW & HyADS)
Lucas sciences paper

## Slide 14
Limitation and future research
Lack of observations available in 1940 and of source-specific pollutants
  Motivate the use of reduced complexity approaches
  Make only indirect evaluation possible
Future work
  Assess the influence of environmental exposures on cognitive decline by linking the exposures with health data
  Explore the exposure to specific pollutants from power plants
  Identify the driving factors of legislation and economics that influenced exposure changes
Notes: LH:
Not interested in CO2 exposure, since it doesn't have health effects
Lack of observations available in 1940 and of source-specific pollutants:
  Motivate the use of reduced complexity approaches
  make only indirect evaluation possible
Future work
  Assess the influence of environmental exposures on cognitive decline by linking the exposures with health data
  Explore the exposure to specific pollutants from power plants
  Identify the driving factors of legislation and economics that influenced exposure changes

## Slide 15
1940 Total PM2.5
1940 Well IDW
1940 Automobile
Other sources’ exposure in 1940
Notes: Make slide for other sources, no necessary go into details, show the major points of each source
LH – recommend showing one map per source (1940 exposure). It is better to show less information and explain it well
It would be helpful if you can come up with a consistent format between this slide and the information in slide 5
Austin:

## Slide 16
Acknowledgment
This project was supported by funding from the National Institute of Health (NIH) grant number R01AG074359.

## Slide 17
Thank you
Questions? xshan2@gmu.edu