## Slide 1: Emissions Methods Improvements to support the NEI and emissions data to support the development of a modeling platform
Tesh Rao
EPA/OAQPS/Emissions Inventory and Analysis Group (EIAG)
October 23, 2024
2024 CMAS Conference

## Slide 2: Other collaborators…
Karl Seltzer, EIAG
Madeleine Strum, EIAG
Yijia Dietrich, EIAG
Rich Mason, EIAG
Lindsay Dayton, EIAG
Alison Eyth, EIAG
Jeff Vukovich, EIAG
Art Diem, EIAG
Jeff Vukovich, EIAG
Jesse Bash, ORD
Amara Holder, ORD
Ingrid George, ORD
Havala Pye, ORD
James Beidler, ORD
George Pouliot, ORD
Kristen Foley, ORD
Nonpoint contractors (David Cooley, Hannah Derrick, Olivia Salmon)

## Slide 3: Topics for Today
Teams in OAQPS’s Emissions Inventory and Analysis Group (EIAG)
  Where does “Methods” and “Science” fit in?
A little background on the NEI
What does the Methods Team do?
What did the methods team accomplish for the 2020 NEI?
How do we use existing tools, data, and input to establish priorities for methods?
Plans for the 2023 NEI
Future work, beyond the 2023 NEI

## Slide 4: Teams in EIAG
NEI (National Emissions Inventory) Team
  Create triennial NEI and annual point source inventories
  Develop new NEI emissions calculation methods & tools
  Sector expertise
  Documentation
  Emission trends and int’l reporting
Emissions Modeling Team
  Create emissions modeling platforms
  Future year emissions projections
  Develop emissions modeling software
  SPECIATE
  Biogenics and model-based emissions
  Documentation
Methods Team
  Climate Pollution Reduction Grant (CPRG) support
  Website & data publishing
  NEI Report
  International reports and custom summaries
  Establishing new methods and improvements to current methods for all sectors and emission trends for NEI and modeling
CAER (Combined Air Emissions Reporting) Team
  Develop new CAER system and associated pieces (feed EIS/TRI)
  Build connections with CEDRI, WebFIRE, and GHG reporting program needed for project
  Implement any AERR revisions that needs CAERS (e.g., direct facility reporting)

## Slide 5: Overview of National Emissions Inventory (NEI) and Related Programs
Emissions Estimation Methods
Emissions Calculation Tools
Emissions Data Collection Tools
Emission Inventories
Emission Modeling Platforms
Emission Trends

## Slide 7: NEI Five Key Goals
Complete: All emissions to the atmosphere included, whether regulated or unregulated, for all counties/tribes including Puerto Rico and the Virgin Islands
Represents the year of the inventory
Uses best available information and the best possible science in EPA methods
Transparent - includes the emissions origin (who provided, factor, activity, method)
Timely
Notes: Fast slide: summarize that v2 release comes down to “good enough” vs policy driver like NATA

## Slide 8: Methods Team – Emission Inventory and Analysis Group
The Methods Team* within EIAG prioritizes areas of the NEI for methodological improvements.
  Improvements can be scientific updates to existing emission sources or the addition of a new source type to the inventory.
  Prioritization accounts for estimated contributions to NAAQS violations, key Hazardous Air Pollutant (HAP) sources, input from stakeholders, and new scientific work suggesting updates necessary for existing methods.
The Methods Team then leads, collaborates on, or incorporates outside work that improves the prioritized items within the inventory development process. This may include emission quantification, future projections, speciation, or temporal and spatial allocation.
  Any work that gets published adds additional credibility to the NEI and downstream uses of NEI
* weblink: https://www.epa.gov/air-emissions-inventories/emissions-science-improvements-emission-sectors

## Slide 9: Sample Emission Methods improvements completed for 2020 NEI
Nonpoint solvent utilization (Karl Seltzer and Havala Pye)
  Complete update, including new emission methods and speciation
  https://acp.copernicus.org/articles/21/5079/2021/
Nonpoint agricultural silage (Tesh Rao)
  New VOC & HAP emissions source
  About 600k tons of VOC nationwide, at cattle/dairy farms
Nonpoint hot-mix and warm-mix asphalt paving added, emulsified/cutback asphalts updated (Karl Seltzer)
  About 85K tons of VOC added
  https://pubs.rsc.org/en/content/articlelanding/2023/ea/d3ea00066d
VOC and PM2.5 speciation updates (Karl Seltzer, George Pouliot, Art Diem)
  Released SPECIATE5.2
    100 or so updated/improved VOC and PM profiles
    Profile type updates and species property updates
Use of Bluesky Pipeline for wildland fire emissions (Jeff Vukovich, James Beidler, George Pouliot)
  More modular approach to estimating emissions
Inclusion of lead (Pb) as a pollutant from wildland fires (Amara Holder and Tesh Rao)
  About 3% of total Pb in the 2020 NEI, nationally. Can be as high as 12-15% in some states
  https://www.sciencedirect.com/science/article/pii/S2590162123000291
Improvements to residential wood combustion PM2.5 emission factors (Madeleine Strum, Rich Mason, NP contractors)
Biogenic model updates (Jesse Bash, Jeff Vukovich)
  Updated emissions factors
  Use of gridded biomass data from USFS
  Improved transition of seasons
  https://gmd.copernicus.org/articles/9/2191/2016/
Use of EQUATES project to upgrade Criteria Air Pollutant Emission Trends (Kristin Foley, George Pouliot, Rich Mason, Alison Eyth, Tesh Rao, many others)
  Established consistent methods over time for many key sectors (2002-2019)
  EPA website: https://www.epa.gov/air-emissions-inventories/air-pollutant-emissions-trends-data
  Manuscript: https://www.sciencedirect.com/science/article/pii/S2352340923001403?via%3Dihub
Find more details on each of these updates, either:
  Via published manuscript
  Or, via 2020 NEI TSD: https://www.epa.gov/air-emissions-inventories/2020-national-emissions-inventory-nei-technical-support-document-tsd

## Slide 10: NEI Drivers - Uses by SLTs
NAAQS and Regional Haze Implementation
  Starting point for State Implementation Plan (SIP) inventory requirements for O3, PM2.5, transport, and regional haze SIPS
    Planning inventories
    Modeling inventories
  NAAQS Designations: emissions (along with monitoring data) are among the most important factors in designation tools used by SLTs (designating non-attainment areas)
NAAQS policy assessments and integrated science assessments (ORD)
EPA works with the SLTs to develop the NEI. We use data submitted by SLTs for all the sources supplemented with estimates that EPA develops

## Slide 11: NEI Drivers - Uses by EPA and Others (1 of 2)
Air quality modeling
  NAAQS Regulatory and Regional Haze: Transport rules, NAAQS Regulatory Impact Analysis (RIA), OTAQ RIAs, international transport
  AirToxScreen – risk results used by SLTs
  Technology Review (RTR): starting point
  ORD air quality model development
  Centers for Disease Control and Prevention (CDC) air quality analysis
  Global modeling inventories used by international community
Emissions trends – national and state
  Air trends report
  ORD Report on the Environment
  International agreements
  Public and press requests
Notes: International examples: (e.g., CLRTAP, US-Canada AQ Agreement, Arctic Monitoring and Assessment Programme (AMAP), Commission for Environmental Cooperation (CEC))

## Slide 12: NEI Drivers - Uses by EPA and Others (2 of 2)
Monitoring: siting purposes
Public information via NEI website
  NEI Report Story Map
  NEI query tools, technical support documentation, submittal instructions, guidance, plan, instructions
  Emissions processes for EPA’s air quality modeling
Data quality analysis
  OECA Enforcement and Compliance History (ECHO) web tool for regulated facilities
  TRI – missing or significant facility differences

## Slide 13: Example of a Key NEI Use: Allocating to hours, grid cells, and species for AQ modeling
Base and Future Inventories (annual, monthly, daily, hourly)
Met. Data
Chart: PM2.5 (tons)
Final product: gridded, hourly, speciated emissions in a format for an air quality model
Temporal Profiles
Speciation Profiles
Spatial Surrogates
SMOKE
SMOKE software system performs temporal allocation, speciation, and spatial allocation to create…
Ancillary Data: profiles and cross references
NEI
where:
  s: sector ranges from broad to specific
  t: time ranging from annual to hourly;
  x: location ranging from state to point
  A: activity data
  EF: emission factor
  CF: control factors
  M: Meteorology
  State-Tribe-Local supersedes EPA where available
NEI Data
Notes: NEI important to international community: methods/factors are often used as example for others

## Slide 14: A few summaries of NEI data
2020 NEI and Trends

## Slide 16
Items to note:
Methods update in 2020 NEI: From 2002-2019, these trends reflect EQUATES-based emissions data, which minimizes time series effects due to method changes
  Stakeholders have indicated this to be a very helpful upgrade
  More sectoral detail available at the national and state level to help explain national trends
  Can isolate more emission sectors
  Added BC and OC
PM2.5 shows static trends over time since 2002, POC shows similar trends
NH3 shows an increasing trend in recent years up to 2020
VOC flattening trends in recent years
Large point source SO2 reductions leading to other sectors playing a role (O&G contributes about 10%) in 2020
Wildfires Omitted
Y-axes represent “Million Tons”

## Slide 17: More things that can be done now with CAP trends with EQUATES-based updates
Chart: RWC, Multi-Pollutant Trends, x1000 tons
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
PM2.5 | 297.76 | 313.43 | 321.27 | 337.14 | 299.01 | 330.48 | 369.83 | 395.62 | 424.3 | 411.54 | 343.9 | 448.74 | 454.14 | 399.83 | 348.15 | 337.23 | 411.42 | 428.28 | 485.08 | 485.08 | 485.08
NOx | 34.67 | 36.49 | 37.41 | 39.25 | 34.81 | 38.48 | 43.06 | 46.06 | 49.4 | 47.92 | 40.04 | 52.25 | 52.88 | 46.55 | 40.54 | 39.26 | 47.9 | 49.87 | 49.79 | 49.79 | 49.79
VOC | 294.09 | 309.56 | 317.3 | 332.97 | 295.32 | 326.4 | 365.26 | 390.73 | 419.06 | 406.46 | 339.65 | 443.2 | 448.53 | 394.89 | 343.85 | 333.07 | 406.34 | 422.99 | 459.88 | 459.88 | 459.88
Black Carbon | 16.62 | 17.49 | 17.93 | 18.81 | 16.68 | 18.44 | 20.64 | 22.08 | 23.68 | 22.96 | 19.19 | 25.04 | 25.34 | 22.31 | 19.43 | 18.82 | 17.25 | 23.9 | 27.07 | 27.07 | 27.07

## Slide 18: Example: PM2.5 and Residential Wood Combustion (RWC)
Chart: PM2.5: 2020 NEI
| Fires | Mobile Nonroad | Mobile Onroad | Misc | Fuel Comb: Non-RWC | RWC | Industrial Processes
 | 2287.9359 | 95.4877 | 71.9049 | 1845.1956 | 316.8916 | 440.0552 | 224.3004
Chart: PM2.5: 2017 NEI
| Fires | Mobile Nonroad | Mobile Onroad | Misc | Fuel Comb: Non-RWC | RWC | Industrial Processes
 | 2010.4521 | 119.888 | 91.5696 | 1965.2579 | 273.6949 | 305.9312 | 244.682
Improved methods to improve RWC (woodstove emissions) in the 2020 NEI, which led to a 44% increase in PM2.5 RWC emissions compared to the 2017 NEI

## Slide 19: Current Methods Priorities List, for 2023 NEI
Roofing Asphalt Emissions (volatile organic pollutants (VOC), HAPs)
  About 12k tons of VOC estimated in 2020 (Nationwide)
Improving commercial cooking emission methods and adding residential cooking (PM2.5, CO, VOC, HAPs)
  Commercial: 330k tons PM2.5, 40k tons VOC, 150k tons CO (2020)
  Residential: 13.5k tons PM2.5, 1.2k tons VOC, 171k tons CO (2020)
Abandoned oil and gas wells (VOC HAP)
  About 174k tons VOC (and about 320k tons CH4) in 2020
NH3 emissions for non-Ag sources (human activities, pets, wild animals), mobile sources
  Uses population and animal population activity data and in sum is nearly equal to what mobile source NH3 estimates are in urban areas
  About 120k tons of NH3 added, mostly in urban areas
  Use updated MOVES model, which will yield ~2x NH3 emissions for onroad
Introduction of structural/motor vehicle fires (CAP, HAP)
  Together about 25k tons of PM2.5 and about 40k tons of VOC
Introduction of pile burn emissions (all pollutants)
  Small amounts of emissions
Possibly Include dioxins/furan congeners for as many sources as possible
Continued improvements to residential wood combustion methods (activity, emission factors, speciation, SCC rearrangements)—(CAP, HAP)
  Introduction of Campfire emissions (about 2-3% of RWC total PM2.5)
  Potential addition of barrel stoves (“exempt” type appliances)
Continued spatial allocation improvements, temporal allocation improvements, speciation updates

## Slide 20: Further “on the horizon” wish list
General improvements to existing sectors, including improvements to spatial allocation methods, temporal allocations, and VOC and PM speciation
Using top-down data to estimate emissions/improve current emissions
  Estimation of emissions from O&G leaks, methane/VOCs
  NH3 sectors
Solvent usage in O&G operations
Development of HAP emission trends
Other (new) sources
  Dust from coal train open compartment rail operations
  Improving dust estimates, and including wind-blown dust in the NEI
  Fireworks
Working more with international community on emission methods and related items
Working to improve sectors that may play an important role in the new PM NAAQS
  Understanding Woodstove emissions better
  Improving Cooking emission estimates

## Slide 21: The Future
We highly value collaborative improvements to the NEI!
  When we say “NEI,” we mean many things: Emission quantification, projections, speciation, or temporal and spatial allocation (i.e., translating annual, county-level emissions to the gridded products we use in air quality models).
We would also like to pursue new avenues of research to build and evaluate inventories: using top-down methods to constrain, allocate or develop estimates of emissions, PMF/NMF analysis of measurements to understand source attribution, generation of “emission ratios” from field work to evaluate the inventory, etc.
Currently methods improvements and additions are geared towards an NEI process (every 3 years). We would like to see how to streamline this process for interim year inventories (such as modeling platforms)
Please contact us with ideas, data, and for collaborative opportunities
  Tesh Rao (rao.Venkatesh@epa.gov)