## Slide 1: Remote Sensing of Ammonia: how it works and what it can tell us
Karen E. Cady-Pereira1, Jeana Mascio1, Betsy Berry1, Elva Kuai3, Enrico Dammers2
CMAS Conference: October 21-23, Chapel Hill, North Carolina
1. AER, Lexington, Mass
2. TNO, The Netherlands
3. NASA Jet Propulsion Laboratory, Pasadena, California
Notes: Greg has introduced the TROPEES products.

## Slide 2: Sources
Fertilizer Application
Livestock Waste
Principal (80%)
Secondary
Biomass burning
Catalytic converters
Notes: Where does it come from? Sources, PM2.5, can be a significant fraction, deposition, ecosystem disruption, algal blooms. NH3 emissions and concentrations are increasing.

## Slide 3: Impact
Van Damme et al 2021
NH3 concentrations have been increasing globally
Notes: Why do we care? Reacts with the ….to form, PM2.5, can be a significant fraction, deposition, ecosystem disruption, algal blooms. NH3 emissions and concentrations are increasing. AS NOX and SOX dreductions hit their limits,, reducing ammonia provides another option to slow PM 2.5 formation.And it’s increasing, as these trends from the IASI instrument show. current distribution and future trends.

## Slide 4
Infrared Sounders
TES (2004-2018)
On NASA AURA
First NH3 measurements from space
High spectral resolution
Sparse coverage
1:30/13:30 LST overpasses
Interferometer
AIRS (2002-2026)
On NASA AQUA
Global daily coverage coverage
1:30/13:30 LST overpasses
Nearing its end-of-life
Radiometer
CrIS (2012-… )
On NASA/NOAA SNPP, JPSS-1,JPSS-2
Scheduled for JPSS-3 and JPSS-4
Global daily coverage
1:30/13:30 LST overpasses
Interferometer
IASI (2006-… )
On Metop-A/B/C
IASI-NG scheduled for Metop-SG A/B/C
Global daily coverage
9:30/21:30 LST overpasses
Interferometer
Notes: Four instruments, time,TES (high res,sparse,overpass). AIRS (almost done,also 13:30 overpass, global coverage), CrIS same advantages as AIRS, but much lower noise), IASI (European, also global but earlier overpass and thus wasker signas.

## Slide 5
Observations
CrIS Obs
CrIS Obs
No NH3
NH3
H2O
O3
Observation – Forward Model Calculations
Observations
CrIS Obs
No NH3
NH3
H2O
O3
Observation – Forward Model Calculations
Observations
Optimal Estimation for NH3
CrIS Obs
No NH3
Initial Guess
Retrieval
NH3
H2O
O3
Observation – Forward Model Calculations
Observations
For more details see: Shephard M.W. and K. E. Cady-Pereira, AMT, 2015
Detectability is ~ 0.25 ppbv under ideal conditions
Thermal contrast plays an important role
Thermal Contrast: Surface- Air Temperature
NH3 Signal vs TCON
Rodgers, 2000
Notes: Measured radiances,forward model with no NH3, NH3 signal, depends on amount and thermal contrast,

## Slide 6: Frequencies of elevated NH3 occurrences from TES
(Graphic) G. Grullón/Science;
(Data) JPL TES Science Team
TES Megacity Observations
2013-2015
eighteen cities
frequent occurrences of elevated NH3 (>10 ppbv)
Delhi, Kolkata, Dhaka
  Traffic, biomass burning, industry
Lagos: local pollution, biomass burning
Paris: transport from surrounding agricultural areas
https://www.science.org/content/article/here-are-some-world-s-worst-cities-air-quality
Notes: As part of the TES Science Team I conducted an analysis of multiple trace gases over 18 megacities. One statistic I looked at was the frequency of NH3 observations greater than 10 during the 2013-2015 period. There were some expected results.

## Slide 7: CrIS Mean Surface NH3 (2013-2017)
Hot spots correspond to areas with intensive agriculture (US Midwest, Central Valley, Central Asia, northwestern Europe), biomass burning (South America, most of Africa, Siberia), or multiple sources (Indo-Gangetic Plain).
Shephard et al., 2020

## Slide 8
Surface NH3 from CrIS and the AMoN Network
IR Sounders: instantaneous profiles over a footprint at least 14 km in diameter
Good agreement between CrIS and AMoN in spite of sampling differences
Ground measurements: point data at the surface (often two week means)
Aircraft measurements: instantaneous point samples along a spiral or a path
All measurements come with large uncertainties!
Notes: How does sounder data compare to in situ measurements? A problem of scales.

## Slide 9: DISCOVER-AQ validation: Central Valley - winter 2013
Retrieved - Aircraft
Cady-Pereira et al., 2024
Central Valley has some of the highest NH3 levels in the US
… but DAQ period coincided with persistent thermal inversions
thinner BL and cool surface layer complicate retrievals
-43 ppb bias at surface, 2 ppb at 900 hPa
Bias possibly due to vertical distribution and PTR-MS lack of sensitivity above 900 hPa
Total column up to 700 hPa
Total column up to 900 hPa
Aircraft data
PTR-MS
Retrieval appears to be shifting NH3 upwards
Notes: High in situ measurements, but inversions make poor conditions for infrared retrievals;

## Slide 10: Validation of CrIS NH3 using USDA network
Cady-Pereira et al., 2024
Ground network: provided two week means of surface NH3
Radiello passive samplers (AMoN type)
Nine sites, 2018-2020
Intensive dairy activities
CrIS NH3 data:
Co-location: within 15 km
Averaged over two weeks
Cris captures seasonal cycle but misses some NH3 spikes
Magic Valley in Idaho
Notes: USDA set up a network of nine sites in the Magic Valley in Idaho.

## Slide 11: Oversampling and source location
Physical oversampling:
average of all pixels within a grid box (0.02 deg) over a selected period (May-October 2020), weighted by the fraction of the pixel within the box AND the spatial response of instrument in that pixel
trades temporal variability for sharpened gradients
Dairy density
Average CrIS Surface NH3
Areas with a high dairy density correlate well with high NH3.
Some monitoring sites are not located within hotspots.
There are NH3 “clouds” downwind of dairies.
Notes: One issue with sounder data is coarse resolution (typically around 15km) but can be coarser at the edge the swath. Box is 1.5 vs 2.5 deg

## Slide 12: NH3 in the Netherlands
The Netherlands are a small country
External sources also contribute to high NH3 levels
Dutch monitoring networks are sparse and mostly situated in low source areas
AIRS can provide better spatial coverage and consistent data going back to 2002
AIRS data co-located with the LML network sites capture most of the interannual variability evident in the in-situ record
High NH3 amounts have caused excess deposition to waterways and nature reserves, which led to new controls:
  18000 development projects blocked
  planned 50% reduction in livestock
  > massive protests: Dutch nitrogen crisis
Notes: 18 million people; 99.9 million chickens, 11.4 million pigs, 3.8 million head of cattle, 0.8 million sheep and 0.5 million dairy goats; the Netherlands is the world’s second-biggest exporter of agricultural products by value behind the US.
Bordered by Germany and Belgium , which also have large sources of NH3

## Slide 13: NH3 from fires in Southern California
Daily active fire detection and thermal anomaly data from MODIS and VIIRS visible channels
CrIS data show significant enhancement in CO and NH3 during
the September 6-14 period
Imperial Valley
CO
NH3
LA Basin
Active fire period: 09/06-09/14
CO
NH3
2017/09
2020/09
2020/09
2017/09
Notes: These plots are part of a larger study of NH3 from fires in Southern Calfornia.

## Slide 14: Ammonia (NH3) emissions from traffic: COVID lockdown study
Figure modified from Cao et al., 2021
COVID-19 lockdowns provided a natural experiment
Urban area presented elevated NH3 and NO2 before lockdown, but low values for both during the lockdown
This results indicates that a significant fraction of urban NH3 in the LA area is due to vehicles
First satellite-based confirmation that vehicles are an under-recognized source of urban NH3 pollution in Los Angeles.
Area dominated by vehicle emissions
Area dominated by agricultural emissions
Notes: Hansen Cao, o used CrIS data over LA to look at the impact of the COVID shutdown on NH3 in the LA Basin. Describe.Used this data along with TROPOMI NO2 and GEOS-Chem to provide the first estimate of NH3 from transportation from space.

## Slide 15: Estimating emissions from CrIS
Cao et al., 2020
Cao et al. (2020) applied a 4DVar approach using CrIS 2014 data to improve GEOS-Chem estimates of NH3 emissions over CONUS
Total posterior annual anthropogenic emission estimate for CONUS is higher than prior estimate by 51%.
Posterior monthly emission for CONUS increased throughout the whole year
Sensitivity tests: 20-30% reductions in SO2 and NOx emissions led to difference < 4% in posterior
Posterior
4.43 Tg N a-1
2.95 Tg N a-1
Posterior
Prior
Cao et al., 2020

## Slide 16: Trends in source regions from AIRS and IASI
Warner et al., 2017
Van Damme et al., 2021
AIRS: 2002-2013
IASI: 2008-2018
Different instruments types (radiometer vs interferometer), different algorithm (OE vs ML), different parameter (level VMR vs column): very similar spatial pattern in the trends.

## Slide 17: Summary
NH3 concentrations obtained by applying optimal estimation radiances measured by infrared sounders have been validated against in situ networks and aircraft data
These data capture:
  global and regional spatial variability
  seasonal cycles
  NH3 generated by fires
… and can be used to
  locate emission sources
  estimate emissions from traffic
  find trends
  improve model emission inventories
Current and planned IR sounders will provide a data record from 2002 into the 2040s
The NOAA GXS sounder on geostationary GeoXO (planned for 2035) will provide hourly observations over North America

## Slide 18: References
Cady-Pereira, K. E., Guo, X., Wang, R., Leytem, A. B., Calkins, C., Berry, E., Sun, K., Müller, M., Wisthaler, A., Payne, V. H., Shephard, M. W., Zondlo, M. A., and Kantchev, V.: Validation of MUSES NH3 observations from AIRS and CrIS against aircraft measurements from DISCOVER-AQ and a surface network in the Magic Valley, Atmos. Meas. Tech., 17, 15–36, https://doi.org/10.5194/amt-17-15-2024, 2024
Cao,H, et al 2020, Environ. Res. Lett. 15 104082
Cao, H., D. K. Henze, K. Cady-Pereira, B. C. McDonald, C. Harkins, K. Sun, K. W. Bowman, T.-M. Fu, and M, O. Nawaz, 2022. COVID-19 lockdowns afford the first satellite-based confirmation that vehicles are an under-recognized source of urban NH3 pollution in Los Angeles. Environmental Science & Technology Letters 9 (1): 3–9.
Shephard, M. W., Dammers, E., Cady-Pereira, K. E., Kharol, S. K., Thompson, J., Gainariu-Matz, Y., Zhang, J., McLinden, C. A., Kovachik, A., Moran, M., and Bittman, S.: Ammonia measurements from space with the Cross-track Infrared Sounder: characteristics and applications. Atmospheric Chemistry and Physics, 20(4), pp.2277-2302, 2020.
Van Damme, M., Clarisse, L., Whitburn, S. et al. Industrial and agricultural ammonia point sources exposed. Nature, 564, 99–103 (2018). https://doi.org/10.1038/s41586-018-0747-1
Van Damme et al 2021, Environ. Res. Lett. 16 055017
Warner, J. X., R. R. Dickerson, Z. Wei, L. L. Strow, Y. Wang, and Q. Liang: Increased atmospheric ammonia over the world’s major agricultural areas detected from space, Geophys. Res. Lett., 44, doi:10.1002/2016GL072305, 2017.

## Slide 19: Backup slides

## Slide 20: TES/AIRS/CrIS NH3 Algorithm Structure
From each observation:
Radiances
Noise estimate
First guess emissivity from
University of Wisconsin database
From previous retrievals:
Water vapor profiles
Temperature profiles
Surface temperature
Optimal estimation first step
Refinements of
  Surface temperature
  Emissivity
Use radiances for
a priori selection from three possible profiles
Cloud screening
Optimal estimation (Rodgers, 2000):
Find the profile that minimizes difference between measured (CrIS) and calculated forward model (OSS) radiances
Optimal estimation second step
NH3 profiles
Error estimates
Averaging kernels
For more details see: Shephard M.W. and K. E. Cady-Pereira, AMT, 2015

## Slide 21: DISCOVER-AQ validation: Central Valley - winter 2013
AIRS
= Xapriori + AK ( Xaircraft - Xapriori )
Retrieved - Aircraft
Retrieved - Aircraft w/AK
Cady-Pereira et al., 2024
CrIS
Applying the instrument operator
Sample AK
Notes: High in situ measurements, but inversions make poor conditions for infrared retrievals