## Slide 1: US mortality impacts of PM2.5 associated with climate change and variability at midcentury using dynamically downscaled global climate and chemistry in WRF and CMAQ
Surendra Kunwar1
Coauthors: Jared Bowden2, George Milly3, Michael Previdi3, Arlene Fiore4, J. Jason West1
1University of North Carolina at Chapel Hill, Chapel Hill, NC, USA
2North Carolina State Climate Office, Raleigh, NC, USA
3Lamont-Doherty Earth Observatory and Columbia University, Palisades, NY, USA
4Massachussetts Institute of Technology, Cambridge, MA, USA
CMAS 2024
Tuesday October 22, 2024

## Slide 2: Future Climate Change Impacts on PM2.5 Air Quality
Climate change can influence air quality in many ways:
Pathway | Example
Anthropogenic emissions | Warmer summer-> more energy demand for cooling -> more fossil fuel burnt
Natural emissions | Stronger wind -> soil erosion -> release of dust particles Examples: biogenic VOCs, dust, wildfires, sea salt, lightning
Air chemistry | Higher temperature-> accelerated chemical reaction of particles
Meteorology | Less rain -> less washing out of PM Examples: PM ventilation by wind, mixing depth, frontal passage, convection, rain, dry deposition

## Slide 3: Past Studies on Future Climate Change Impacts on US PM2.5
Limitations of some earlier regional modeling studies:
  downscaled global model to regional scale using single realization of one model to simulate PM2.5 changes
  averaged 5-10 years’ PM2.5 values to represent period of interest
  may not have accounted for climate variability
Important to understand the context of climate variability in climate-change impact studies

## Slide 4: Climate Variability vs Climate Change in a Global Model
PM2.5 variability+change illustrated by 3 GFDL ensemble members H1 and H3 at an arbitrary US location:
NATURAL CLIMATE VARIABILITY = fluctuation around a steady mean
CLIMATE CHANGE (SIGNAL) = long term change of mean
≠
+
NATURAL FORCING = caused by solar activity, volcanoes
INTERNAL VARIABILITY (NOISE) = internally arising due to chaotic nature of climate system
Internal Variability (noise) can confound Climate Change (signal):
US location (red dot) for which GFDL ensemble PM2.5 is shown

## Slide 5: Study Objective
‘To quantify the impacts of RCP8.5 climate change (in the 2050s compared to the present) and variability on US PM2.5 and related human mortality at fine spatial resolution, using a novel approach of combining probability distributions from multi-year global model ensembles with downscaling over the continental US.’
GFDL model
WRF model
CMAQ model
Year 2006-2100
8 selected years dynamically downscaled
3 ens. members
6 hourly output
2.5o X 2.5o grid
Hourly output
12km grid
8 selected years downscaled
Hourly output
12km grid
BenMAP-CE
Health impacts of downscaled years calculated
8 years selected
meteorology
meteorology
chemistry
emissions
SMOKE processor
air quality
Notes: We use different models to achieve this objective – which we show as a flowchart in next slide.

## Slide 6: Steps Towards Constructing Probability Distribution of PM2.5 associated Mortality at Fine Scale using Global and Regional Models
3-ensemble, coarse Global Chemistry-Climate Model simulations for 2006-2100 under RCP8.5 scenario
Select 8 GCM years representing high/median PM2.5
Dynamical downscaling of meteorology (WRF 12km)
Air quality downscaling (CMAQ 12km) with inline biogenic, lightning NOx, seasalt emissions
Construct fine scale probability distribution of mean annual PM2.5 change between present and future
Study associated probabilistic impacts of PM2.5 variability on human health
Study associated probabilistic impacts of climate induced PM2.5 changes on visibility
Notes: Emphasize (1) 8 years are selected from GCM (2) third project will be about visibility

## Slide 7: WRF/CMAQ Simulations
Scenario Name | Time | Meteorology | GFDL IC/BC | Anthropogenic Emissions | # Realizations
PRES | 2006-2020 | 2005 RCP8.5_WMGG | RCP8.5_WMGG | 2016 National Emissions Inventory (NEI) | 4
FUT | 2051-2065 | 2050 RCP8.5_WMGG | RCP8.5_WMGG | 2016 National Emissions Inventory | 4
Land Use/Cover remains constant for all WRF/CMAQ simulations
GFDL RCP8.5_WMGG fixes aerosol, precursor emissions at 2006 level
CMAQ simulations use 2016 NEI emissions to reflect current emissions
FUT - PRES = effect of only climate change on future PM2.5
Simulations conducted in regional models WRF and CMAQ:

## Slide 8: WRF Physics Options
8 selected GFDL years (RCP8.5 meteorology with 2005 emissions) downscaled in WRFv3.8.1.1:
12km domain
36km domain
Parameter | Physics options used in WRF simulation
mp_physics = 6 | WSM 6-class graupel scheme microphysics
ra_lw_physics = 4 | RRTMG radiative transfer scheme for longwave radiation
ra_sw_physics = 4 | RRTMG radiative transfer scheme for shortwave radiation
sf_surface_physics = 2 | Unified Noah land-surface model
cu_physics = 1 | Kain-Fritsch (new Eta) scheme for cumulus parameterization
num_land_cat = 40 | 40 land categories of NLCD2011 used
num_soil_cat = 16 | 16 categories of soil data
Domains used in Simulations
Physics Options used in WRFv3.8.1.1 simulations
* Spectral nudging is applied to moisture for better precipitation results (Spero et al, 2018)

## Slide 9
GFDL vs WRF 2m Temperature : July 2058 (ens. H1) Example
General 2-m temperature [T2; units of Kelvin] patterns of GFDL simulations represented in WRF
WRF simulation adds fine scale details
 | T2 July 2058(H1) Maximum | T2 July 2058(H1) Minimum | T2 July 2058(H1) Mean
GFDL 2058 H1 |  |  | 
WRF 12km |  |  | 

## Slide 10
GFDL vs WRF Monthly Precipitation Total: July 2058 (ens. H1)
GFDL 2058 H1
WRF 12km
  General precipitation [units mm] pattern of GFDL are represented well in WRF*
  WRF simulation adds finer scale details in precipitation
* Spectral nudging applied to moisture in WRF simulations for better precipitation results (Spero et al, 2018)
* July-December 6-month spinup used for surface temperature IC for better Inland lake model results

## Slide 11: CMAQ Simulation Setup
12km CONUS domain adopted
Meteorology-sensitive emissions used inline in CMAQ:
  sea spray aerosol emission
  lightning NOx emissions
  biogenic emissions
CMAQ O3 BC and IC from GFDL modified:
  ozone (O3) overestimation bias-corrected for better matching with observations

## Slide 12: GFDL vs CMAQ vs Observation PM2.5
CMAQ PM2.5 is mostly underestimated at regional level (West coast and Southeast):
 | GFDL (μg/m3) | CMAQ 12k (μg/m3) | FRM Observation (μg/m3)
2006 (H1 ens. member) |  |  | 
2054 (H5 ens. Member) |  |  | 

## Slide 13: Mean-scaling: Connecting GFDL and CMAQ Annual Average Statistics of PM2.5
To estimate distribution of mean annual PM2.5 in fine scale, Mean-scaling method used:
CMAQ distribution mean (by applying above mean-scaling method):
CMAQ distribution standard deviation (applying mean-scaling):
With mean and stdev. are estimated, PM2.5 normal distribution is defined.
Mean-scale factor
*
*

## Slide 14: FUT–PRES PM2.5 Distribution from Monte Carlo Samples
AVG of FUT-PRES calculated by Monte Carlo Sampling
STDEV of FUT-PRES calculated by Monte Carlo Sampling
The mean (left below) and the stdev. (right below) describe the probability distribution (assumed Gaussian) of FUT-PRES mean annual PM2.5:

## Slide 15
Regional Trends of ΔPM2.5 Components
PM2.5 mean increase is the highest in
  Southern US (50 x 50 CMAQ gridcells aggregated around AL), and
  Ohio River Valley (50 X 50 CMAQ gridcells aggregated around TN)
Temperature-led increase in OC is only partly offset by decrease in nitrate component in both regions
Southeast US
Ohio River Valley

## Slide 16: Gridcell-specific Results of Mean-scaling of PM2.5: Charlotte, NC
Mean-scaling of the Average and Stdev. of PRES and FUT annual PM2.5 describe the Gaussian distribution of mean annual PM2.5at each gridcell
Similarly, health effects of PM2.5 due to climate change can be extrapolated in individual gridcells over CONUS domain

## Slide 17: Mean Scaling Method for Estimating Annual PM2.5 related Mortalities Distribution ~ N(µ,σ)
- CMAQ Gaussian distribution parameters of annual mortalities calculated at each gridcell assuming:
averaged
averaged
averaged
Mean Scale Factor
GFDL 45-years’ (3 ensemble members times 15 years) binned annual mortality averages
GFDL 4 selected years’ annual mortality average
CMAQ 4 selected years’ annual mortality average
- CMAQ distribution std. dev. () is obtained from:
- Once are calculated, PM2.5 normal distribution is defined!
CMAQ distribution mortalities (estimate of DESIRED QUANTITY )

## Slide 18
PM2.5 Human Health Impacts Distribution due to Climate Change
Illustration of steps to estimate present-day annual mortalities distribution at single gridcell (hypothetical):
1a) Histogram of GFDL based health mortalities
4) Estimated Gaussian fit to CMAQ
1b) Gaussian fit to GFDL histogram
2) Selected 4 GFDL years’ annual mortalities
Similar steps taken to estimate midcentury annual mortalities distribution
Impact of climate change on human mortality due to PM2.5 changes estimated by Monte Carlo sampling from present and future distributions
3) Corresponding 4 CMAQ years’ mortalities

## Slide 19: Preliminary Result from BenMAP: PRES-FUT Distribution of Mean Deaths at Gridcell Level
‘PRES-FUT PM2.5 distribution mean’ health impacts over CMAQ 12k grid:
Population used: US Census based 2015 population (available within BenMAP)
HIF used: study by Krewski et al., 2009

## Slide 20: Preliminary Result from BenMAP: PRES-FUT Distribution Mean Deaths Aggregated at State Level
‘PRES-FUT PM2.5 distribution mean’ health impacts over CMAQ 12k grid:
CONUS aggregated excess deaths in 2050s compared to the present: 8,712

## Slide 21: Conclusion
We quantified climate change impacts on US PM2.5 in 2050s compared to present, in the presence of climate variability, by:
  using ensemble global model simulation to characterize PM2.5 variability,
  downscaling meteorology and air quality in selected years to fine resolution (12km),
  keeping anthropogenic emissions constant
  mapping fine scale probability distributions of PM2.5 in individual grid cells
Our novel method:
  generated probabilistic information about climate change+variability induced PM2.5 changes in individual grid cells
  is also being used in health impacts of PM2.5 due to climate change and climate variability at fine resolution
Future steps:
  fit different probability distribution models to health impacts of PM2.5 to see resulting climate change impact
  aggregate FUT-PRES PM2.5 health impacts over multiple gridcells (e.g. of a city)
  apply similar approach to visibility

## Slide 22: Acknowledgment
My PhD Advisor, Collaborators/coauthors, Mentors, Committee, Lab group
NSF’s XSEDE program and UNC Research Computing for computational resources
USEPA (STAR grant #RD83587801), Weiss Urban Livability Fellowship (Graduate School), Don and Jennifer Holzworth Fellowship (Environmental Sciences and Engineering) for funding
LDEO Fiore group (then at Columbia University) for GFDL data; Gus Correa for GFDL data transfer support

## Slide 23: Thank You for listening!
Questions/Comments