## Slide 1: Dynamic Coupling of Meteorologically-induced (MetEmis) NH3 Livestock Emissions with CMAQv5.4
CMAS 2024, Chapel Hill, NC
Bok. H. Baek, Siqi Ma, Chi-Tsan Wang, Youhua Tang, Patrick Campbell, and Daniel Tong
George Mason University
NOAA JTTI (Joint Technology Transfer Initiative) Project

## Slide 2: Dynamic Coupling of MetEmis Emission Sources
Meteorologically-induced Emission (MetEmis) Coupler Module that allows dynamically estimate emissions with local meteorological conditions
  Onroad Mobile Emissions
  Agricultural Livestock Emissions
Process-based Emissions Models are needed for dynamical coupling with the CTM systems
  U.S. MOVES that estimates spatiotemporal emissions as function of vehicle-fuel-specific emissions factors, various traffic activities and local ambient temperature and humidity
  Farm Emissions Model (FEM) that estimates NH3 and VOC emissions as a function of animal-specific emission factors, animal population, farm management practices, and local ambient temperature, wind speed, and precipitations
Not practical to compute emissions from MetEmis sources as an inline module within the CTM due to its complex data requirements and computational resource requirements
CMAQ-MetEmis: Dynamic MetEmis Coupler Module for CMAQ
  CMAQ-MetEmis_MB for Moblile Sources
  CMAQ-MetEmis_LV for Livestock Waste Sources

## Slide 3: CMAQ-MetEmis
Developed a new CMAQ inline coupler for Meteorologically-induced Emissions sources (MetEmis)
MetEmis_TBL: Pseudo-layered Temperature-bin Gridded Hourly Emissions (Not Emission Factors)
Dynamically estimate the emissions by interpolating the gridded emissions between the temperature-bins
No computational burden for CMAQ to process Pseudo-layered Temperature-bin Gridded Hourly emissions
Completed CMAQ-MetEmis_MB development based on MOVES Emissions
  Show the MPE improvement on finer spatial resolution CTM simulations
For Livestock waster sector, followed the same MetEmis approach with additional met variable of precipitation which could lower the NH3 emissions
(Baek et al., GMD 2023)

## Slide 4: Gas-to-Particle Conversion between NH3, and Acid Gases
Ammonia: NH3
Most alkaline pollutants in the atmosphere neutralize the acid gases
Acid Gases: H2SO4, HNO3 and HCl
Acidification of soils and acid rains
Mostly from anthropogenic emissions
Fine Particles: PM2.5
Formed from reactions with Ammonia and Acid Gases
Key emission sector to control the secondary inorganic aerosol (SIA)
But, unlike many controlled emissions, NH3 emissions from livestock waste is projected to grow in the future
(Stiles, Farming Connect, 2020)

## Slide 5: Farm Emission Model (FEM)
Manure types : Dairy, Cattle, Poultry and Swine
  Nitrogen Inputs (manure and urine), Dryness of excretion, Surface for housing /storage, Runoff area,,,,
  pH plays a critical role in NH3 from housing and storage
Management Practices
  Housing: tiestall, freestall, deep/shallow-pit, manure-belt,,,,
  Storage: lagoon, earthbasion, and slurry tank
  Application: irrigation, injection, training hose, broadcast
  Grazing: seasonal, monthly, weekly, daily.
Meteorology
  Temperature  NH3 emissions
  Wind speed  NH3 emissions
  Precipitation  NH3 emissions
(Pinder et al., 2004)

## Slide 6: FEM Submodel Data Flow Diagram
Nitrogen and water
From literature or previous submodel
Submodel
(e.g. swine storage)
Daily Average Emission Factor
Inputs
Outputs
Nitrogen and water balance
(goes to next submodel)
Adjusted parameters
Meteorological data
(temp., WS, precip)
EF = {A*[TAN]*H} / r
r = ra + rb + rs
ra =Aerodynamic resistances
rb =Quasi-laminar resistance
rs = Surface resistance: Tuned to match measured EFs from observations
Hutchings et al (1996) A model of NH3 volatilization from a grazing livestock farm
For confined animal housing:
﻿rs = H1 + H2T
For Beef open feedlots housing:
rs = H1T + H2u + C
: H1 and H2 are constants and tuned to capture variability due to temperature and wind speed
FEM has been used for the official livestock waste emission sector for U.S. EPA NEI since 2014

## Slide 7: Contributors of NH3 Emissions in the U.S. (2019)
(?)
(?)

## Slide 8: NH3 Bottom-up vs Top-down Emissions Comparison
Spatially difference distribution between BU and TD NH3 annual total emissions
Temporal trends of NH3 are different by region due to the seasonal meteorological condition
Indicating that the significant differences over the Great Plains and Southwest regions
Quantitively questionable due to the uncertainties of NOAA CrIs NH3 retrievals
US NEI NH3 | Top-Down NH3
(Baek and Xing, ITM, 2023)

## Slide 9: Sector-level NH3 Emissions Comparison (2020)
Beef Cattle
Swine
Bottom-up
Top-down
Diff (TD-BU)
(Baek and Xing, ITM, 2023)

## Slide 10: Seasonal Spatial Distribution of [NH3] b/n Satellite and CMAQ
(Shepard et al., 2020)
2020 CMAQ [NH3]
2020 NH3 Emissions
2020
2020
Notes: In winter time, much less NH3 emissions over the domain but especially under represented especially in the mid-US. In July summer, same lack of NH3 emissions while over NH3 conc from Iowa and NC. Overall, CA NH3 looks reasonable while over estimates of NH3 from IOWA and NC and under-estimated of NH3 from Mid-US.

## Slide 11: Spatial Distribution of [NH3] from AMoN and CMAQ
2017 AMoN [NH3]
NADP, 2024
Mid-US: Under-estimated NH3
UT: Extreme under-estimated NH3
IA & NC: High Over-estimated NH3
CA: Equivalent NH3
Notes: In winter time, much less NH3 emissions over the domain but especially under represented especially in the mid-US. In July summer, same lack of NH3 emissions while over NH3 conc from Iowa and NC. Overall, CA NH3 looks reasonable while over estimates of NH3 from IOWA and NC and under-estimated of NH3 from Mid-US.

## Slide 12
Mid-US Under-estimated NH3 emissions
Illinois Indiana Kansas Texas
Utah
North Carolina
California
Black: Base Red: MetEmis
2020 AMoN vs [NH3]
Notes: CA where shows consistent high NH3 emissions shows a good correlation with AMoN NH3 conc. While IL, KS, UT state AMoN shows a significant underestimate which is consistent to the findings from NOAA CrIS NH3 conc distribution as well as AMoN observations

## Slide 13: Summary [1]
Over-estimated NH3 emissions from Swine CAFOs in the Iowa and NC
  Revisit the calibrating/updating the NH3 emission factors (grams/animal)
  Assess the detailed impacts of precipitation on Swine over the Eastern U.S.
Under-estimated NH3 emissions from the Beef Cattle in the mid-U.S.
  Current approach is based on NH3 EF x Animal Populations
  Lack of representing the size of beef cattle open feedlots with meteorological impacts
  Need an update of FEM to improve the size of sources and the wind speed impacts on open feedlots
These over/under-estimations of NH3 findings are consistent with the findings from the top-down NH3 Inverse modeling method

## Slide 14: NH3 Emission Changes (MetEmis-Base)
Notes: Unlike we witnessed in earlier slides, there are significant impacts on NC eastern area NH3 increase due to the higher ambient temperature.

## Slide 15: NH3 Concentration Changes (MetEmis-Base)

## Slide 16: Seasonal Concentrations

## Slide 17: MetEmis Impacts on NH3 and PM2.5

## Slide 18: Summary and Future Works
MetEmis impacts on NH3 can be greater during the winter season when higher NOx emissions are emitted.
What is next?
  Once the spatial distribution of NH3 emissions from the livestock waste sector is updated, model performance will be evaluated with AQS dataset
  Dynamic coupling of NH3 emissions from the Livestock Waste sector could improve their spatiotemporal representations within the CTM system
  Plan to add the wind-speed layers to the MetEmis_TBL for Livestock, which is critical to the emissions from the application and especially from beef cattle open feedlot

## Slide 19: Acknowledgement
  U.S. NOAA Joint Technology Transfer Initiative (JTTI)
  U.S. EPA OAQPS
  Ministry of Environment in Korea